Report for : Mark Calicutt / Sam Falkner

Compiled by : Mark Smith

| WELL | CBA F27 |
| --- | --- |
| DATE | 25-05-2009 |
| REPORT # | 19 |
| MIDNIGHT ACTIVITY | Back reaming out of hole at 901.0 mMDRT. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3983.0 mMDRT |  | MINIMUM | - | - |
| TVD | 2465.6 mTVDRT |  | MAXIMUM | - | - |
| PROGRESS LAST 24 hrs | 0.0 m |  | AVERAGE | - | - |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance | 3436.0 | 2184.7 | -2143.7 | 0.3 H | 3449.6 | 2185.0 |
| Top of Latrobe Group | 3769.5 | 2356.4 | -2315.4 | 4.4 L | 3773.9 | 2352.0 |
| Top Coarse Clastics | 3772.5 | 2357.9 | -2316.9 | 3.9 L | 3777.8 | 2354.0 |
| Top M101B Upper Reservoir | 3781.5 | 2362.5 | -2321.5 | 7.5 L | 3779.7 | 2355.0 |
| Top M101D Upper Reservoir | 3785.5 | 2364.5 | -2323.5 | 5.5 L | 3787.5 | 2359.0 |
| Top M101D Lower Reservoir | 3797.0 | 2370.4 | -2329.4 | 6.4 L | 3797.2 | 2364.0 |
| Top M101E Reservoir | 3811.0 | 2377.6 | -2336.6 | 4.6 L | 3814.7 | 2373.0 |
| M111 Reservoir | 3828.0 | 2386.3 | -2345.3 | 1.3 L | 3838.0 | 2385.0 |
| M131 Reservoir | 3887.0 | 2416.5 | -2375.5 | 0.5 L | 3898.2 | 2416.0 |
| Total Depth | 3983.0 | 2465.7 | -2424.7 | 6.1 L | 3982.8 | 2459.6 |

| Current Formation |  |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | - | - | - | - | - | - | - | - |
| MAX (GFF) | - | - | - | - | - | - | - | - |
| BG (Reserval) | - | - | - | - | - | - | - | - |
| BG (GFF) | - | - | - | - | - | - | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 7 | 6 |
| SIZE (in) | 9-7/8 | 9-7/8 |
| MANUFACTURER/TYPE | Reed Hycalog / RSD616M | Mill Tooth |
| JETS (/32 inch) | 6 x 18 | 3 x 22 |
| DEPTH IN (m) | 603.0 | 599 |
| DEPTH OUT (m) | - | 603 |
| METRES ON RUN (m) | 3380.0 | 4 |
| HRS ON BTM 24hrs/total | 69.2 | 0.0 / 0.6 |
| BIT CONDITION | - | - |
| RPM RANGE 24hrs |  | - |
| Pump Hrs 24 hrs / total | 14.1 / 130.0 | 0 / 14.2 |
| Krevs 24 hrs / total | 575 | 0 / 2 |

| 24 HOUR SUMMARY | Back ream out of hole at 5 minutes a stand from 2815.0 mMDRT to 901.0 mMDRT, flow check at 1952.0 mMDRT. |
| --- | --- |
| 26-05-2009 5AM UPDATE | Back ream out of hole at 5 minutes a stand from 901.0 mMDRT to 585.0 mMDRT. Circulate hole clean, flow check and pump slug. Pull out of hole from 585.0 mMDRT to 352.0 mMDRT. 5AM DEPTH: 3983.0 mMDRT (2465.6 mTVDRT) |