Culverin-1

| Date: | 1-01-2006 | Last Casing: | 340 mm (13 3/8”) @ 1511.14 mMDRT |
| --- | --- | --- | --- |
| Report Number: | 13 | Leak Off Test: | 1.89 sg EMW @ 1528.0 mMDRT |
| Report Period: | 24hrs to 24:00 | Current hole size: | 311 mm (12 1/4”) |
| Depth @ 2400 Hrs: | 3571.0 mMDRT | Mud Weight: | 1.22 sg |
| Last Depth: | 3473.0 mMDRT | ECD: | 1.22 sg |
| Progress: | 98 m | Mud Type: | KCl-NaCl-Polymer |
| TD Lithology: | Siltstone, Coal and Argillaceous Sandstone | Mud Chlorides: | 84, 000 ppm |
| Water Depth: | 585.0 m | Mud Fluid Loss: | 3.6 cc |
| RT Elevation: | 21.5 m | Bit Type: | PDC (Reed-Hycalog) |

OPERATIONS SUMMARY

| 24 HOUR SUMMARY 00:00 - 24:00: | Drilled ahead from 3473.0 mMDRT to 3571.0 mMDRT. POOH for suspected washout. |
| --- | --- |
| 06:00 Update | Pull out of the hole from 85 mMDRT and inspect BHA for washouts. |
| NEXT 24 HOURS: | Inspect BHA for washouts. Down load LWD. RIH and drill ahead 311 mm (12 ¼”) hole. |

GEOLOGICAL SUMMARY

- LITHOLOGIC DESCRIPTION:

| Interval mMDRT | Description |
| --- | --- |
| 3475 – 3510 ROP 5.2-76 m/hr Ave 20 m/hr | Argillaceous Sandstone, Sandstone (only at 3530m sample), Siltstone and thin Coals in an interbedded sequence. ARGILLACEOUS SANDSTONE (40-80%): 60% white aggregates to 40% clear translucent loose grains, fine to coarse, dominantly fine to medium, moderately sorted, sub-angular to angular, moderate sphericity, 70% white argillaceous matrix in aggregates, fair to moderate inferred porosity, no fluorescence. (3505m) SANDSTONE (70%): 50% white aggregates 50% loose grains, dominantly fine to medium, occasionally coarse, moderately well sorted, sub angular to rounded, high sphericity, common white argillaceous matrix, trace pyrite nodules and cement, good inferred porosity, no fluorescence. SILTSTONE (15-60): light brownish grey, brownish grey, off white / light brownish grey, very soft to rarely friable, very argillaceous, carbonaceous specks and carbonaceous laminae in part, slightly pyritic in part. Sample from 3490.0 mMDRT contained hard siliceous and pyritic Siltstone. COAL (Trace-5%): black, dull black, sub vitreous, firm, blocky, silty in part. |
| 3510 – 3550 ROP 0.8-30 m/hr Ave 10 m/hr | Argillaceous Sandstone, Siltstone and common Coal in an interbedded sequence. Trace Fluorescence present at 3515.0 mMDRT (see fluorescence summary below). ARGILLACEOUS SANDSTONE (10-80%): white to very light grey, soft aggregates, trace loose grains, very fine to fine, occasional medium grains, moderately well sorted, sub-angular to angular, white argillaceous matrix to 80% (possibly weathered feldspars?), poor inferred porosity, no fluorescence (except trace at 3515.0 mMDRT see fluorescence summary below). SILTSTONE (20-90%): light brownish grey, brownish grey, light grey, very soft, rarely sub-firm, amorphous to sub-blocky, rarely sub-fissile, trace carbonaceous specks and carbonaceous laminae, occasionally pyritic, occasionally very pyritic, trace very hard black & white finely banded siliceous fragments. COAL (Trace-5%): dull black, sub vitreous, firm, brittle in part, hackly fracture, very silty in part and gradational to carbonaceous siltstone. (Based on the LWD logs the thin coals probably make up 20% of the entire section but are under-represented in the cuttings samples). |
| 3550 – 3565 0.7 – 10.5 m/hr Ave 4.5 m/hr | Dominantly Siltstone with minor Argillaceous Sandstone and thin Coals. SILTSTONE (80-90%): light brownish grey, brownish grey, occasionally white, very soft, amorphous to dispersive, very argillaceous, common carbonaceous specks and carbonaceous laminae, occasionally pyritic, trace very hard black & white finely banded siliceous fragments. ARGILLACEOUS SANDSTONE (10-20%): white to very light grey, loose grains, very fine to fine, occasional medium grains, well sorted, sub angular to angular, white argillaceous matrix to 80% (weathered feldspars?), poor inferred porosity, no fluorescence. COAL (Trace): dull black, sub vitreous, firm, brittle in part, hackly fracture, very silty in part and gradational to Carbonaceous Siltstone. |

- HYDROCARBON FLUORESCENCE:

| INTERVAL (mMDRT) | FLUORESCENCE |
| --- | --- |
| 3510-3515 | Trace dull yellow, trace very slow cut, trace dull cream incomplete residue ring. Fluorescence occurred in white Argillaceous Sandstone. |

- GAS SUMMARY:

| INTERVAL (mMDKB) | Total GAS (%) | C1 (ppm) | C2 (ppm) | C3 (ppm) | IC4 (ppm) | NC4 (ppm) | C5 (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3475 – 3510 | 0.75 | 5572 | 483 | 153 | 36 | 46 | 12 |
| 3510-3565 | 1.32 | 10210 | 904 | 279 | 69 | 63 | 26 |
| 3484 PEAK | 0.86 | 6237 | 655 | 199 | 35 | 56 | 54 |
| 3501 PEAK | 1.68 | 14751 | 1070 | 289 | 53 | 48 | 60 |
| 3518 PEAK | 2.10 | 16208 | 1318 | 377 | 79 | 64 | 41 |
| 3533 PEAK | 3.01 | 22869 | 1491 | 351 | 117 | 68 | 36 |
| 3543.5 PEAK | 3.72 | 15315 | 1223 | 589 | 136 | 98 | 28 |

- SURVEYS

| MD | ANGLE | Azi |  | MD | ANGLE | Azi |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2743.83 | 3.80 | 42.10 |  | 3375.03 | 3.69 | 54.03 |  |  |
| 2772.65 | 3.83 | 43.73 |  | 3404.40 | 3.54 | 54.90 |  |  |
| 2801.66 | 3.84 | 42.76 |  | 3432.80 | 3.59 | 51.96 |  |  |
| 2830.44 | 3.89 | 43.81 |  | 3461.32 | 3.48 | 51.53 |  |  |
| 2859.14 | 3.95 | 44.31 |  | 3490.24 | 3.38 | 50.31 |  |  |
| 2887.70 | 3.86 | 45.65 |  | 3519.26 | 3.32 | 50.11 |  |  |
| 2916.43 | 3.87 | 45.26 |  | 3547.59 | 3.32 | 49.95 |  |  |
| 2944.96 | 3.83 | 45.79 |  |  |  |  |  |  |
| 2973.53 | 3.73 | 46.71 |  |  |  |  |  |  |
| 3002.19 | 3.72 | 46.75 |  |  |  |  |  |  |
| 3059.49 | 3.72 | 46.57 |  |  |  |  |  |  |
| 3088.21 | 3.81 | 46.46 |  |  |  |  |  |  |
| 3116.08 | 3.75 | 45.37 |  |  |  |  |  |  |
| 3145.07 | 3.74 | 48.33 |  |  |  |  |  |  |
| 3173.79 | 3.67 | 49.59 |  |  |  |  |  |  |
| 3202.65 | 3.71 | 48.97 |  |  |  |  |  |  |
| 3231.77 | 3.53 | 48.2 |  |  |  |  |  |  |
| 3260.37 | 3.66 | 49.86 |  |  |  |  |  |  |
| 3346.36 | 3.65 | 50.41 |  |  |  |  |  |  |
| 3375.03 | 3.69 | 54.03 |  |  |  |  |  |  |

- WELLSITE GEOLOGISTS:

| Mike Woodmansee | Rob Blackmore |
| --- | --- |

- FORMATION TOPS

| WD = 585.0 m RTE = 21.5 m |
| --- |
| FORMATION | PROGNOSED DEPTHS (m) | ACTUAL DEPTHS (m) |
|  | MDKB | TVDSS | THICK | MDKB | TVDSS | HI/LO | THICK | DIFF |
| Sea Floor/ Gippsland Limestone | 607 | 585 | 1975 | 606.5 | 585.0 | 0.0 | 1899.9 | 0.0 |
| Lakes Entrance | 2582.0 | 2560.0 | 325 | 2508.0 | 2484.9 | 75.1 H | 315.1 | -10.0 |
| Latrobe | 2907.0 | 2885.0 | 30 | 2824.0 | 2800.0 | 85.0 H | 11.0 | -19.0 |
| Base TF Channel | 2937.0 | 2915.0 | 10 | 2835.0 | 2811.0 | 104.0 H | 1.0 | -8.0 |
| Top 67.5 Ma Sand | 2947.0 | 2925.0 | 310 | 2836.0 | 2812.0 | 113.0 H | 266.5 | -43.5 |
| Near 68.5 Ma Sand | 3257.0 | 3235.0 | 226 | 3103.0 | 3078.5 | 156.5 H | 374.3 | -148.3 |
| Near 70.3 Ma Sand | 3482.5 | 3461.0 |  | 3478 | 3452.8 | 8.2 H |  |  |
| Near 74 Ma Sand | Not prog |  |  |  |  |  |  |  |
| TD | 3612.0 | 3590.0 |  |  |  |  |  |  |

- COMMENTS:

Sperry-Sun LWD sensor to bit distances: (same LWD toolstring run following bit trip)

Directional = 13.13 m

Gamma-Ray = 15.73 m

Resistivity = 18.04 m

Density = 25.66 m

Porosity = 30.97 m

ACAL = 29.93 m