| WELL: Glenaire-01 | REPORT No.: | 22 | DAYS FROM SPUD: | 22 | DATE: | 30/09/06 |
| --- | --- | --- | --- | --- | --- | --- |
| PL: PEP 160 | 0000 hrs Depth: | 3230 m | LAST DEPTH: | 3230 m | PROGRESS: | 0 m |
| LOCATION: Otway Basin | Rig: Ensign 32 | RT elevation: | 76.1 m | PTD: | 3945 m |
| Northing: 5 840 813 m N | Easting: 499 810 m E | Ground Level | 70.0m |  |  |
| NEARBY WELLS: | Tullich-1, Mceachern-1, Haselgrove South-1, Heathfield-1 |
| 0600 OPS: Drill ahead to 3247m. |
| PREVIOUS 24 Hours Operations: RIH, circulate hole clean (WTG 3076 units (81:8:7:3:1)), POOH, pick up bent sub and steering assembly to correct excessive hole deviation, RIH, TG 3790u, orientate tool, prepare to drill ahead. |
| Comment: Controlled drilling to correct excessive hole deviation. Mud weight increased to 10.0 ppg due to increased formation pressure. |

| Formation Tops | Wellsite | Wellsite | Prognosed Depths | Prognosis |  |
| --- | --- | --- | --- | --- | --- |
| (Wellsite) | (mRT) | (mSS) | (mRT) | (mSS) | Diff H/L |  |
| Gambier Limestone | 6.1 | 70 | 6 | 70 | 0 |  |
| Dilwyn Formation | 29 | 47 | 82 | -6 | 53H |  |
| Pember Formation | 320 | -244 | 347 | -271 | 27H |  |
| Pebble Point Formation | 380 | -304 | 421 | -345 | 41H |  |
| Sherbrook Group | 448 | -372 | 487 | -411 | 39H |  |
| Eumeralla Formation | 609 | -533 | 656 | -580 | 47H |  |
| Windermere/Katnook Ss | Not Present | n/p | 2034 | -1958 | Not Present |  |
| Laira Formation | 1968 | -1892 | 2059 | -1983 | 91H |  |
| Pretty Hill Formation |  |  | 3746 | -3670 |  |  |
| T.D. |  |  | 3945 | -3869 |  |  |

| Interval (m) ROP (ave) min/m | Lithology Description | Gas/Background Breakdown C1/C2/C3/C4/C5 |
| --- | --- | --- |
| 3230 – 3246 (5) | SILTY CLAYSTONE, (90%) medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, (10%) off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace fine black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 35 – 462 (95) (79:8:7:4:2) |
| Fluorescence | The sandstone has dull orange mineral fluorescence, no cut. The detrital coal has no fluorescence but gives a very weak dull yellow crush cut. |

| Fluorescence |  |
| --- | --- |

| Fluorescence |  |
| --- | --- |

| Fluorescence |  |
| --- | --- |

| Fluorescence |  |
| --- | --- |

| Fluorescence |  |
| --- | --- |

| Fluorescence |  |
| --- | --- |

| Fluorescence |  |
| --- | --- |