DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS MARCH 6, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 291 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 213 | 213 |
| CAMERON | 1766 | 1766 |
| HALLIBURTON | 3570 | 3570 |
| SCHLUMBERGER | 2475 | 2475 |
| ISS | 283 | 2357 |

Well: HLA_A16

Rig/Contractor: 	Rig 453	Report Date: March 6, 2007

Supervisor:	Smith, Gary G

Campbell, Glenn R

| AFE Number: AFE Number: | L0501H210 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days on AFE | 6.3 | AFE Cost/Days: | $6,614,569 |
| Daily Cost: | $241,332 |  |  |
| Total Cost: | $1,222,739 | Planned MD/TVD: | 2,535.30 / 3,012.05 |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | HLA_A16 |
| --- | --- |
| Management Summary: | PTSM's. Held fire, power choke & trip drills. M/u & RIH with 8-1/2" cleanout BHA. Pressure test 10-3/4" surface casing to 1000 psi. Drillout cement in surface casing from 400m to 549m. Pump sweep & circulate hole clean. Conduct PIT to 12.4 ppg MWE - no leakoff. C/out damaged TDS saver sub. Displace well to 9.3 ppg KCL/PHPA/Polymer mud. POH & l/out cleanout BHA. M/u 8-1/2" steerable drilling BHA with PDC bit. M/u motor, MWD & LWD tools. Set motor bend. Shallow test tools. RIH with BHA on 5" HWDP. |
| Current: | RIH w/ steerable drilling BHA on 5" HWDP. |
| Planned: | RIH w/ steerable drilling BHA to 549m. Kickoff & drill 8-1/2" production hole. |

DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS MARCH 6 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 291 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 213 | 213 |
| CAMERON | 1766 | 1766 |
| HALLIBURTON | 3570 | 3570 |
| SCHLUMBERGER | 2475 | 2475 |
| ISS | 283 | 2357 |

Well: FTA _A12a

Rig/Contractor: 	Rig 175	Report Date: March 6 2007

Supervisor:	Steel, George

Moss, Ross

Stead, Cory

| AFE Number: AFE Number: | L0501H000 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days on AFE | 53.5 | AFE Cost/Days: | $10,210,000 |
| Daily Cost: | $185,468 |  |  |
| Total Cost: | $9,363,927 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | FTA_A12a |
| --- | --- |
| Management Summary: | Continue R/U for BOP testing. Unable to achieve shell test on stack - bonnets leaking. R/dn BOP test assembly. Lost 2.25 Hrs due to installation of modified centre board - unable to rack 5½" drill pipe w/ original centre board. P/U, drift & rack 5½" drill pipe. |
| Current: | P/U & racking 5½" DP. |
| Planned: | Continue w/rig up operations. P/U & rack 5½" drill pipe. Test BOP's. |