DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS MARCH 8, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 293 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 215 | 215 |
| CAMERON | 1768 | 1768 |
| HALLIBURTON | 12 | 3570 |
| SCHLUMBERGER | 2477 | 2477 |
| ISS | 285 | 2357 |

Well: FTA_A12A

Rig/Contractor: 	Rig 175	Report Date: March 8, 2007

Supervisor:	Stead, Cory

Steel, George A

Morris, Ross B

| AFE Number: AFE Number: | L0501H001 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days on AFE | 0.21 | AFE Cost/Days: | $8,661,510 |
| Daily Cost: | $37,459 |  |  |
| Total Cost: | $37,459 | Planned MD/TVD: | 4,033.00 / 3,342.35 |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | FTA_A12a |
| --- | --- |
| Management Summary: | Refer to Rig Mobilization report #56 for operations from 05:00 Hrs, March 7 to 00:00 Hrs, March 8. Continue testing BOP's w/ 4" test assembly. Test TIW's, Gray valves, 4" pipe rams & annular. |
| Current: | Breaking down & L/out 4" test assembly. |
| Planned: | Cont. R/U ops. Commission rig. Offload SBM. |

DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS MARCH 8, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 293 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 215 | 215 |
| CAMERON | 1768 | 1768 |
| HALLIBURTON | 12 | 3570 |
| SCHLUMBERGER | 2477 | 2477 |
| ISS | 285 | 2357 |

Well: FTA _A12a

Rig/Contractor: 	Rig 175	Report Date: March 8 2007

Supervisor:	Stead, Cory

Steel, George A

Morris, Ross B

| AFE Number: AFE Number: | L0501H000 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days on AFE | 55.54 | AFE Cost/Days: | $10,210,000 |
| Daily Cost: | $149,838 |  |  |
| Total Cost: | $9,543,457 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | FTA_A12a |
| --- | --- |
| Management Summary: | Continue pressure testing BOP's to 250 psi low & 5000 psi high w/ 5½" & 4" test assemblies. Test annular, rams, choke manifold, standpipe manifold, cement manifold, choke & kill HCV and TDS. Complete grating installation on pipe deck. Transfer to Drill Well AFE at 00:00 Hrs. See Drilling & Completion report #1 for operations from 00:00 Hrs to 05:00 Hrs. |
| Current: | Transfer to Drill Well AFE at 00:00 Hrs, Mar 8/07 |
| Planned: | See Drilling & Completion report #1. |

DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS MARCH 8, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 293 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 215 | 215 |
| CAMERON | 1768 | 1768 |
| HALLIBURTON | 12 | 3570 |
| SCHLUMBERGER | 2477 | 2477 |
| ISS | 285 | 2357 |

Well: HLA_A16A

Rig/Contractor: 	Rig 453	Report Date: March 8, 2007

Supervisor:	Bigby, Brigham

Campbell, Glenn R

| AFE Number: AFE Number: | L0501H210 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days on AFE | 8.13 | AFE Cost/Days: | $6,614,569 |
| Daily Cost: | $240,070 |  |  |
| Total Cost: | $2,709,655 | Planned MD/TVD: | 2,535.30 / 3,012.05 |
| Casing Size: |  | Actual MD/TVD: | 1,163.00 / |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | HLA_A16A |
| --- | --- |
| Management Summary: | PTSM's. Held pit drills. Drill, steer & survey 8-1/2" production hole from 749m to 1142m. Rig service. Drill, steer & survey 8-1/2" production hole from 1142m to 1163m. |
| Current: | Drill 8-1/2" production hole. |
| Planned: | Continue to drill, steer & survey 8-1/2" production hole. |