DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS November 29, 2006

| RIG 453 | 194 | 363 |
| --- | --- | --- |
| CAMERON | 1669 | 1668 |
| HALLIBURTON | 3456 | 3455 |
| SCHLUMBERGER | 2398 | 2397 |
| ISDL | 194 | 647 |
| ISS | 182 | 2357 |

Well: HLA_A24

Rig/Contractor: 	Rig 453	Report Date: November 29, 2006

Supervisor:	Campbell, Glenn R.

Brigham Bigby

Stead, Cory

| AFE Number: | LO501G206 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 28.0 | AFE Cost/Days: | $6,713,761 |
| Daily Cost: | $163,066 |  |  |
| Total Cost: | $4,787,624 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | HLA_A24 |
| --- | --- |
| Management Summary: | PTSM & hazard hunts. Continue installing mud pumps & mud system spoolwork & hoses. Continue to r/up rig floor. Assist electrician & Mechanic power up generator & rig hydraulics. Arrange decks, unload equipment & prepare backloading. Work boats & backload as required. Lift & secure BOP's on link plates. Reeve drilling line through blocks to drawworks & secure line. Commenced installing airlift hoses. Install mast section 1 & pin to crown ready for scoping. R/u scoping slings & bridle. HLA crane shutdown at 03:45 Hrs due to weather. WKF crew completed final washdown of platform & demanned. CBA crew serviced Lady Kari-Ann as required & continued cleaning & servicing equipment. |
| Current: | Rig up scoping slings & bridle. |
| Planned: | Continue general rig up operations. Scope mast weather permitting. |