DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS FEBRUARY 6, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 263 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 185 | 185 |
| CAMERON | 1738 | 1738 |
| HALLIBURTON | 3542 | 3542 |
| SCHLUMBERGER | 2447 | 2447 |
| ISS | 255 | 2358 |

Well: HLA_A24

Rig/Contractor: 	Rig 453	Report Date: February 6, 2007

Supervisor:	Campbell, Glenn R

Bareswill, JR (Dicky)

| AFE Number: AFE Number: | L0501G208 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days on AFE | 13.5 | AFE Cost/Days: | $6,507,763 |
| Daily Cost: | $240,539 |  |  |
| Total Cost: | $2,921,045 | Planned MD/TVD: | 2,984.99/ |
| Casing Size: |  | Actual MD/TVD: | 1,528,.00/ |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | HLA_A24 |
| --- | --- |
| Management Summary: | PTSM's. Held pit drills & fire drill. Drill, steer & survey 8-1/2" production hole from 1180m to 1291m. Rig service. Replace damaged TDS torque beam anchor post bolts. Drill, steer & survey 8-1/2" production hole from 1291m to 1528m. |
| Current: | Drill 8-1/2" production hole. |
| Planned: | Continue to drill, steer & survey 8-1/2" production hole. |

DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS FEBRUARY 6, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 263 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 185 | 185 |
| CAMERON | 1738 | 1738 |
| HALLIBURTON | 3542 | 3542 |
| SCHLUMBERGER | 2447 | 2447 |
| ISS | 255 | 2357 |

Well: FTA _A12a

Rig/Contractor: 	Rig 175	Report Date: February 6, 2007

Supervisor:	Davis, Brian

Bennett, James

| AFE Number: AFE Number: | L0501H000 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days on AFE | 24.71 | AFE Cost/Days: | $10,210,000 |
| Daily Cost: | $179,958 |  |  |
| Total Cost: | $4,255,758 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | FTA_A12a |
| --- | --- |
| Management Summary: | PTSM's.Install pit level indicators. Fit east pump module stairs. Continue w/ spooling and pipe manifold installation. Reinstate DSM fire/gas alarms. Continue w/ exhaust lagging. Modify roller brackets for set back trolly. Install valves @ mud tanks. Install pit level indicators. Service Far Scandia: Unload truss section and process module. Install/pin same. Continue to service boat. Unload BOP test stump/skid beam ramp, BOP transport skid. Truss extension w/ walkway. |
| Current: | Service Far Scandia |
| Planned: | Continue rig up operations. |