DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS JANUARY 18, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 244 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 167 | 167 |
| CAMERON | 1719 | 1719 |
| HALLIBURTON | 3523 | 3523 |
| SCHLUMBERGER | 2428 | 2428 |
| ISS | 236 | 2357 |

Well: HLA_A2B

Rig/Contractor: 	Rig 453	Report Date: January 18, 2007

Supervisor:	Stead, Cory

Steel, George A

| AFE Number: AFE Number: | L0501G207 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 18 | AFE Cost/Days: | $5,677,031 |
| Daily Cost: | $206,596 |  |  |
| Total Cost: | $4,433,659 | Planned MD/TVD: | 3,299.00/3,058.68 |
| Casing Size: |  | Actual MD/TVD: | 3,347.00/2,450.59 |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | HLA_A2B |
| --- | --- |
| Management Summary: | Complete N/U BOP's. M/U 2-7/8" test assembly. Test VBR's & Annular to 300/3000 psi for 5 mins. Test casing to 300/3000 psi for 15 mins. R/U & run gauge ring/junk basket. POOH. RIH w/ HSD guns, correlate on depth & perforate. M/U 7" casing scraper & RIH to 232m. |
| Current: | RIH w/ 7" casing scraper at 232m. |
| Planned: | RIH to 3314m working casing scraper as per program. Circulate well to ISW. POOH w/ 7" scraper. R/U & run 2-7/8" tandem completion. |