DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS FEBRUARY 1, 2007

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| ISDL RIG 453 | 258 | 363 |
| --- | --- | --- |
| ISDL RIG 175 | 180 | 180 |
| CAMERON | 1733 | 1733 |
| HALLIBURTON | 3537 | 3537 |
| SCHLUMBERGER | 2442 | 2442 |
| ISS | 250 | 2357 |

Well: HLA_A4

Rig/Contractor: 	Rig 453	Report Date: February 1, 2007

Supervisor:	Bennett, James

Bigby, Brigham

| AFE Number: AFE Number: | L0501G208 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 8.5 | AFE Cost/Days: | $6,507,763 |
| Daily Cost: | $208,637 |  |  |
| Total Cost: | $1,745,709 | Planned MD/TVD: | 2,984.99/ |
| Casing Size: |  | Actual MD/TVD: | 553.00/ |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | HLA_A24 |
| --- | --- |
| Management Summary: | PTSM's. Drill 12 1/4" surface hole from 553m to 641m. Circulate 2 bottoms up. POOH from 641m to 165m. RIH from 165m to 641m. Circulate bottoms up and pump 30Bbl hi-vis pill. POOH from 641m to surface and L/out BHA. R/up and RIH w/ 9 5/8" casing to 225m. Conduct rig service. Work Kari-Anne from 00:30 hrs to 04:00 hrs. Work Scandia from 04:00 hrs to 06:00 hrs. |
| Current: | RIH w/ 9 5/8" casing @ 225m. |
| Planned: | RIH and cement 9 5/8" casing. |