LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Hazelwood-1 | REPORT No. : | 37 | DFS: | 36 | DATE : | 29-04-07 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 2081m | LAST DEPTH : | 2081m | 24 HR PROGRESS: | TD | PTD : | 2,081m |
| TOTAL FUEL : |  | FUEL USAGE : |  | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Set surface plug from 35m to surface- Layed out Kelly- Rigging down BOP for removal from wellhead |
| Next 24 Hrs Op | Remove BOP and Wood group “ B “ section –secure well-dump and clean mud tanks then release the Rig |
| Site Personnel: | Lou De-Vattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number |  |  |  | Drilling |  |  | Density |  | S.G. |
| Size (mm) |  |  |  | Tripping | 16.00 |  | Viscosity |  | Sec |
| Make |  |  |  | Surveys |  |  | Water Loss |  | Cc |
| Type |  |  |  | Sip & Cut block line |  |  | pH |  | Strip |
| IADC Code |  |  |  | Wash and ream |  |  | Filter Cake |  | 32 nd |
| Serial Number |  |  |  | Circulate Sample |  |  | PV / YP |  | Cp/lb/100’ |
| Nozzles (32) |  |  |  | Casing |  |  | Gels |  | S/m |
| Depth in (m) |  |  |  | Cementing | 1.50 |  | Sand |  | % Vol |
| Depth out (m) |  |  |  | BOP |  |  | Solids |  | % Vol |
| Total Metres |  |  |  | Circulate & Condition | 0.50 |  | Oil |  | % Vol |
| Hours |  |  |  | Rig Service |  |  | K+ |  | Mg/l |
| WOB (kg) |  |  |  | Lay out BHA | 3.50 |  | Chlorides |  | Mg/l |
| RPM |  |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition |  |  |  | Repair rig |  |  | KCL |  |  |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ | 0 |
| Jet Velocity |  |  |  | Logging | 2.50 |  | Cum Cost $ | 55,001 |
| B.H.A.: |  |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 39.5@108 | ° at | 1628 | m |  | Type | Amount |
| 0000 | 02:00 | Ran log # 3 sonic-temp -nav |  | 43 @ 110 A | ° at | 1722 | m |  | Aus-Gel |  |
| 02:00 | 02;30 | Rigged down logger |  | 45@ 113 A | ° at | 1778 | m |  | Pac L |  |
| 02:30 | 05:00 | Tripped in hole with open ended drill pipe to 1321m |  | 40@ 114 A | ° at | 1874 | m |  | Pac - R |  |
| 05:00 | 06:00 | Rigged up Halliburton-safety meeting –tested lines |  | 40@112 A | ° at | 1950 | m |  | Barite |  |
| 06:00 | 06:30 | Set 70m plug # 1 from 1321m to 1248m |  | 48@ 110 A | ° at | 2069 | m |  | PHPA/ KCL |  |
| 06:30 | 07:00 | Pulled back to 1200m |  |  | ° at |  | m |  | Caustic Soda |  |
| 07:00 | 07:30 | Reversed out |  |  |  |  |
| 07:30 | 09:00 | Tripped out to 628m |  | PUMP 1 |  | PUMP 2 |
| 09:00 | 12:00 | Layed out drillpipe |  | Liner | 108 | mm |  | Liner | 108 | mm |
| 12:00 | 14:30 | Tripped in hole to 1276 tagged top of cement mplug |  | Pressure |  | kPa |  | Pressure |  | KPa |
| 14:30 | 20:30 | Layed out drill pipe |  | A.V. DP |  | f/min |  | A.V. DP |  | f/min |
| 20:30 |  | Ran 4 collars in hole –picked up Kelly –removed |  | A.V. DC |  | f/min |  | A.V. DC |  | f/min |
|  | 23:00 | Kelly spinner-bushings- tong breaked connections |  | SPM |  |  | SPM |  |
| 23:00 |  | Layed out 4 drill collars- tested casing against plug with |  | GPM |  |  | GPM |  |
|  | 24:00 | 3500kpa |  |  |  |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton | 900 |  | Size | 244 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 36 | Lb/ft |
|  |  |  |  | % |  |  |  | Grade | K-55 |  |
|  |  |  |  | % |  |  |  | Connection | B.T.C |  |
|  |  |  |  | % |  |  |  | Joints | 110 |  |
|  |  |  |  | % |  |  |  | Length | 1291.00 | m |
| Days since | LTA | 337 |  | Av. Wt |  |  | Shoe | 1296m from RKB | m |

,66