HENRY 2DW1:  CUTTINGS SAMPLE DESCRIPTIONS

| Depth From (m) | Depth To (m) | % | Lithology and Shows |
| --- | --- | --- | --- |
| HENRY 2 was spudded on 25th August 2008 utilising the semi submersible drilling facility "Ocean Patriot". Note: all returns were to the seafloor prior to running the 340mm (13 3/8") casing, blow out preventer and marine riser at 657m. The 311mm (12 ¼") hole section was drilled to total depth at 2042m MDRT. Henry 2 was plugged back and sidetracked as Henry 2DW1 from 1652m at 05:00 hours on 16th September 2008. |
| 1611 | 1628 | 100 | Soft Cement Time drill from 1628m attempting to sidetrack 05:00hrs 100% Cement |
| 1628 05:30hr |  | 70 30 | Cement Siltstone |
| 1629 06:00hr |  | 90 10 | Cement Siltstone |
| 1629.8 06:30hr |  | 90 10 trace | Cement Siltstone Sandstone |
| 1630 07:00hr |  | 70 30 | Cement Siltstone |
| 1630.4 07:30hr |  | 60 40 | Cement Siltstone |
| 1630.5 08:00hr |  | 40 60 trace | Cement Siltstone Sandstone |
| 1631.6 08:30hr |  | 60 40 trace | Cement Siltstone Sandstone |
| 1632.4 09:00hr |  | 60 40 trace | Cement Siltstone Sandstone |
| 1632.8 09:30hr |  | 60 40 trace | Cement Siltstone Sandstone |
| 1633.3 10:00hr |  | 70 30 trace | Cement Siltstone Sandstone |
| 1633.5 10:30hr |  | 40 60 trace | Cement Siltstone Sandstone, common nodular pyrite. |
| 1634.0 11:00hr |  | 75 25 | Cement Siltstone |
| 1634.4 11:30hr |  | 50 50 trace | Cement Siltstone, common nodular pyrite. Sandstone |
| 1634.6 12:00hr |  | 40 60 | Cement Siltstone, occasional nodular pyrite. |
| 1634.9 12:30hr |  | 40 60 | Cement Siltstone, occasional nodular pyrite. |
| 1635.3 13:00hr |  | 50 50 trace | Cement Siltstone Sandstone |
| 1636.1 13:30hr |  | 60 40 | Cement Siltstone |
| 1636.5 14:00hr |  | 70 30 | Cement Siltstone |
| 1636.6 14:30hr |  | 30 70 trace | Cement Siltstone Sandstone |
| 1637.1 15:00hr |  | 40 60 trace | Cement Siltstone Sandstone |
| 1637.2 15:30hr |  | 30 70 trace | Cement Siltstone Sandstone |
| 1637.8 16:00hr |  | 40 60 | Cement Siltstone |
| 1638.0 16:30hr |  | 30 50 20 | Cement Siltstone Sandstone |
| 1640.0 17:30hr |  | 20 40 40 | Cement SILTSTONE: medium to dark grey to grey brown, minor arenaceous, occasional glauconite grains and carbonaceous specks, moderately hard to hard, blocky to sub-blocky. SANDSTONE: off white, clear to translucent in part, very fine to fine, minor medium, moderately well sorted, sub-angular to dominantly sub-round, weak calcareous cement, common off white argillaceous matrix, common rock flour, loose, friable to moderately hard in part, poor to very poor visual & inferred porosity, no fluorescence. |
| 1641.0 19:00hr |  | 20 60 20 | Cement Siltstone Sandstone |
| 1641.0 19:30hr |  | 20 70 10 | Cement Siltstone Sandstone |
| 1641.1 20:00hr |  | 20 70 10 | Cement Siltstone Sandstone |
| 1641.7 20:30hr |  | 30 60 10 | Cement Siltstone Sandstone |
| 1643.0 21:00hr |  | 20 70 10 | Cement Siltstone Sandstone |
| 1643.9 21:30hr |  | 20 60 20 | Cement Siltstone Sandstone |
| 1644.3 22:00hr |  | 20 80 trace | Cement Siltstone Sandstone |
| 1645.0 22:30hr |  | 20 80 trace | Cement Siltstone Sandstone |
| 1645.1 23:00hr |  | 20 60 20 | Cement Siltstone Sandstone |
| 1645.6 23:30hr |  | 30 60 10 | Cement Siltstone Sandstone |
| 1645.8 24:00hr |  | 30 30 40 | Cement Siltstone Sandstone |
| 1646 00:30hr |  | 20 60 20 | Cement Siltstone Sandstone |
| 1646.7 01:00hr |  | 40 40 20 | Cement Siltstone Sandstone |
| 1647.09 01:30hr |  | 20 40 40 | Cement Siltstone Sandstone |
| 1647.50 02:00hr |  | 20 40 40 | Cement Siltstone Sandstone |
| 1648.0 02:30hr |  | 20 40 40 | Cement Siltstone Sandstone |
| 1648.8 03:00hr |  | 20 30 50 | Cement Siltstone Sandstone |
| 1648.8 03:30hr |  | 10 40 50 | Cement SILTSTONE: medium dark grey, medium to dark brownish grey, argillaceous in part, minor to common glauconite, trace nodular pyrite, trace carbonaceous flecks, moderately hard, sub blocky. SANDSTONE: off white, very light brown, translucent, clear, fine to occasionally medium grained, sub angular to predominately sub rounded, moderately sorted, trace calcareous cement, common off white argillaceous matrix, (rock flour ?), trace nodular pyrite, trace glauconite, friable aggregates, poor inferred porosity, no fluorescence. |
| 1650.0 04:00hr |  | 10 30 60 | Cement Siltstone Sandstone |
| 1651.5 04:30hr |  | 5+ 30 70 | Cement SILTSTONE: medium dark grey, medium to dark brownish grey, argillaceous in part, very finely arenaceous in part, rare to common glauconite, trace micro mica, trace carbonaceous flecks, moderately hard, sub blocky. SANDSTONE: off white, very light brownish grey, translucent, clear, very fine to fine grained, trace medium, sub angular to predominately sub rounded, moderately well sorted, common weak calcareous cement, common off white argillaceous matrix, (rock flour ?), rare glauconite, friable aggregates, poor inferred porosity, no fluorescence. |
| 1651.80 05:00hr |  | tr - 5 30 70 | Cement Siltstone Sandstone |
|  |  |  | Henry 2DW1 sidetracked from the Henry 2 well from 1652m at 05:00 hours on 16th September 2008 |
| 1652 | 1654 | trace -3 30 70 | Cement SILTSTONE: medium dark grey, medium to dark brownish grey, argillaceous in part, very finely arenaceous in part, rare to common glauconite, trace nodular pyrite, trace micro mica, trace carbonaceous flecks, moderately hard, sub blocky. SANDSTONE: off white, very light brownish grey, translucent, clear, very fine to fine grained, trace medium, sub angular to predominately sub rounded, moderately well sorted, common weak calcareous cement, common off white argillaceous matrix, , rare glauconite, friable aggregates, poor inferred porosity, no fluorescence. |
| 1654 | 1657 | 20 80 | SILTSTONE: medium dark grey, medium to dark brownish grey, argillaceous in part, very finely arenaceous in part, rare to common glauconite, trace nodular pyrite, trace micro mica, trace carbonaceous flecks, moderately hard, sub blocky. SANDSTONE: off white, very light brownish grey, translucent, clear, very fine to fine grained, sub angular to predominately sub rounded, well sorted, common weak calcareous cement, common off white argillaceous matrix, trace glauconite, friable aggregates, poor inferred porosity, no fluorescence. |
| 1657 | 1660 | 10 90 | SILTSTONE: medium grey to grey brown, occasionally pale to dark brown grey, argillaceous to arenaceous, occasional glauconite grains, moderately hard to occasionally hard, sub-blocky to minor blocky. SANDSTONE: clear to translucent, pale brown in part, very fine to very well sorted, sub-angular to dominantly sub-round, weak calcareous cement, minor pale brown to off white argillaceous matrix, generally loose clean grains, minor friable, poor visual porosity, poor to occasionally fair inferred porosity, no fluorescence. |
| 1660 | 1670 | 60 40 | SILTSTONE: pale brown, occasionally pale to dark brown grey, argillaceous to minor arenaceous, occasional glauconite grains and carbonaceous specks, moderately hard to occasionally hard, very soft to dispersive in part, sub-blocky to minor blocky, amorphous in part. SANDSTONE: clear to translucent, pale brown in part, very fine to fine, occasionally medium, moderately sorted, sub-angular to dominantly sub-round, weak calcareous cement, minor pale brown to off white argillaceous matrix, generally loose clean grains, minor friable, poor visual porosity, poor to occasionally fair inferred porosity, no fluorescence. |
| 1670 | 1680 | 80 20 | SILTSTONE: pale brown, occasionally pale to dark brown grey, argillaceous, rare glauconite grains, minor carbonaceous specks, very soft to dispersive, minor moderately hard, amorphous, sub-blocky to minor blocky. SANDSTONE: off white, clear to translucent, very fine to fine, occasionally medium, moderately sorted, sub-angular to dominantly sub-round, weak calcareous cement, common off white argillaceous matrix, generally loose clean grains, minor friable, poor visual and inferred porosity, no fluorescence. |
| 1680 | 1690 | 100 | SILTSTONE: pale brown, minor medium to dark brown grey, argillaceous, minor carbonaceous specks, very soft to dispersive, minor moderately hard, amorphous, sub-blocky to minor blocky. |
| 1690 | 1700 | 100 | SILTSTONE: pale brown, minor medium to dark brown grey, argillaceous, minor pyrite nodules and carbonaceous specks, very soft to dispersive, minor moderately hard, amorphous, sub-blocky to minor blocky. |
| 1700 | 1710 | 100 | SILTSTONE: pale brown to pale grey brown, minor medium to dark brown grey, argillaceous, minor glauconite grains, very soft to dispersive, minor firm to moderately hard, amorphous, sub-blocky to minor blocky. |
| 1710 | 1720 | 100 | SILTSTONE: pale brown, occasionally medium to dark grey brown, generally argillaceous, minor arenaceous, occasional glauconite grains and pyrite nodules, dominantly very soft to dispersive, firm to moderately hard in part, amorphous, sub-blocky. |
| 1720 | 1730 | 100 | SILTSTONE: pale brown, occasionally medium to dark grey brown, generally argillaceous, minor arenaceous, occasional to common carbonaceous specks, dominantly very soft to dispersive, firm to moderately hard in part, amorphous, sub-blocky. |
| 1730 | 1740 | 100 | SILTSTONE: pale brown, occasionally medium grey brown, generally argillaceous, minor arenaceous, occasional to common carbonaceous specks, minor glauconite grains, dominantly very soft to dispersive, firm to moderately hard in part, amorphous, sub-blocky. |
| 1740 | 1750 | 80 20 | SILTSTONE: pale brown, occasionally medium grey brown, generally argillaceous, minor arenaceous, occasional to common very fine carbonaceous specks, minor glauconite grains, dominantly very soft to dispersive, firm to moderately hard in part, blocky to sub-blocky. SANDSTONE: off white, clear to translucent, very fine, trace fine, moderately well sorted, sub-angular to dominantly sub-round, weak calcareous cement, common off white argillaceous matrix, friable, trace loose clean grains, poor visual and inferred porosity, no fluorescence. |
| 1750 | 1760 | 100 | SILTSTONE: medium brown, occasionally medium grey brown, generally argillaceous, minor arenaceous, occasional to common carbonaceous specks, minor glauconite grains, dominantly very soft to dispersive, firm to moderately hard in part, amorphous, sub-blocky. |
| 1760 | 1770 | 100 | SILTSTONE: pale brown, occasionally medium grey brown, generally argillaceous, minor arenaceous, occasional to common carbonaceous specks, minor glauconite grains, dominantly very soft to dispersive, firm to moderately hard in part, amorphous, sub-blocky. |
| 1770 | 1780 | 100 | SILTSTONE: pale to medium brown, occasionally medium grey brown, generally argillaceous, minor arenaceous, occasional to common carbonaceous specks, minor glauconite grains, dominantly very soft to dispersive, firm to moderately hard in part, blocky to sub-blocky, amorphous in part. |
| 1780 | 1790 | 100 | SILTSTONE: pale to medium brown, grey brown, generally argillaceous, minor arenaceous, occasional to common carbonaceous specks, minor glauconite grains, dominantly soft to firm, minor dispersive & amorphous, blocky to sub-blocky. |
| 1790 | 1800 | 70 30 | SILTSTONE: medium brown, medium grey, dark brown grey, argillaceous, common glauconite grains, minor very fine carbonaceous specks, rare nodular pyrite, trace micro-micaceous, soft to firm, minor moderately hard, sub-blocky to minor blocky. SANDSTONE: off white, clear to translucent, very fine to fine, moderately well sorted, sub-angular to rounded, trace calcareous cement, trace off white argillaceous matrix, generally loose clean grains, minor friable, poor visual and inferred porosity, no fluorescence. |
| 1800 | 1810 | 80 20 | SILTSTONE: medium grey brown, medium grey, dark brown, argillaceous, trace arenaceous, common glauconite grains, minor very fine carbonaceous specks, trace nodular pyrite, trace light brown LIMESTONE fragments, trace micro-micaceous, soft to moderately hard, sub-blocky to blocky, trace amorphous. SANDSTONE: off white, clear to translucent, very fine to medium grained in part, dominantly fine grained, moderately well sorted, sub-angular to sub-rounded, trace calcareous cement, trace off white argillaceous matrix, generally loose clean grains, minor friable, poor visual and inferred porosity, no fluorescence. |
| 1810 | 1820 | 80 20 | SILTSTONE: medium grey brown, medium grey, dark brown, argillaceous, trace arenaceous, common glauconite grains, minor very fine carbonaceous specks, trace nodular pyrite, trace light brown LIMESTONE fragments, trace micro-micaceous, soft to moderately hard, sub-blocky to blocky, trace amorphous. SANDSTONE: off white, clear to translucent, very fine to medium grained in part, dominantly fine grained, moderately well sorted, sub-angular to sub-rounded, trace calcareous cement, trace off white argillaceous matrix, generally loose clean grains, minor friable, poor visual and inferred porosity, no fluorescence. |
| 1820 | 1830 | 80 20 | SILTSTONE: medium grey brown, medium grey, dark brown, argillaceous, trace arenaceous, common glauconite grains, minor very fine carbonaceous specks, trace nodular pyrite, trace light brown LIMESTONE fragments, trace micro-micaceous, soft to moderately hard, sub-blocky to blocky, trace amorphous. SANDSTONE: off white, clear to translucent, very fine to medium grained in part, dominantly fine grained, moderately well sorted, sub-angular to sub-rounded, trace calcareous cement, trace off white argillaceous matrix, generally loose clean grains, minor friable, poor visual and inferred porosity, no fluorescence. |
| 1830 | 1840 | 80 20 | SILTSTONE: medium grey brown, medium grey, dark brown, argillaceous, trace arenaceous, common glauconite grains, minor very fine carbonaceous specks, trace nodular pyrite, trace light brown LIMESTONE fragments, trace micro-micaceous, soft to moderately hard, sub-blocky to blocky, trace amorphous. SANDSTONE: off white, clear to translucent, very fine to medium grained in part, dominantly fine grained, moderately well sorted, sub-angular to sub-rounded, trace calcareous cement, trace off white argillaceous matrix, generally loose clean grains, minor friable, poor visual and inferred porosity, no fluorescence. |
| 1840 | 1850 | 60 40 | SILTSTONE: medium grey, grey brown, brown, argillaceous, trace arenaceous, trace glauconite grains, minor very fine carbonaceous specks, trace light brown LIMESTONE fragments, trace micro-micaceous, soft to moderately hard, sub-blocky to blocky, trace amorphous. SANDSTONE: off white, clear to translucent, light grey, very fine to fine grained, trace medium, moderately well sorted, sub-angular to sub-rounded, trace matrix, generally loose clean grains, minor friable, poor visual and inferred porosity, no fluorescence. |
| 1850 | 1860 | 90 10 | SILTSTONE: light to medium grey, grey brown, brown, argillaceous, trace arenaceous, trace glauconite grains, minor very fine carbonaceous specks, trace light brown LIMESTONE fragments, trace micro-micaceous, soft to moderately hard, sub-blocky to blocky, trace amorphous. SANDSTONE: off white, clear to translucent, very fine to fine grained, moderately well sorted, sub-angular to sub-rounded, trace calcareous cement, trace off white argillaceous matrix, generally loose clean grains, minor friable, poor visual and inferred porosity, no fluorescence. |
| 1860 | 1870 | 100 | SILTSTONE: medium grey brown, light to medium grey, dark brown, argillaceous, trace arenaceous, common glauconite grains, minor very fine carbonaceous specks, rare nodular pyrite, rare light brown LIMESTONE fragments, trace micro-micaceous, soft to moderately hard, sub-blocky to blocky, trace amorphous. |
| 1870 | 1880 | 90 10 | SILTSTONE: medium grey, grey brown, brown, argillaceous, trace arenaceous, trace glauconite grains, minor very fine carbonaceous specks, trace light brown LIMESTONE fragments, trace micro-micaceous, trace pyrite nodules, soft to moderately hard, sub-blocky to blocky, trace amorphous. SANDSTONE: off white, clear to translucent, very fine to fine grained, trace medium grained, moderately well sorted, sub-angular to sub-rounded, trace calcareous cement, trace off white argillaceous matrix, generally loose clean grains, minor friable, poor visual and inferred porosity, no fluorescence. |
| 1880 | 1890 | 100 | SILTSTONE: medium grey brown, light to medium grey, dark brown, argillaceous, trace arenaceous, common glauconite grains, minor very fine carbonaceous specks, rare nodular pyrite, rare light brown LIMESTONE fragments, trace micro-micaceous, soft to moderately hard, sub-blocky to blocky, trace amorphous. |
| 1890 | 1900 | 100 | SILTSTONE: medium grey brown, medium grey, dark brown, argillaceous, trace arenaceous, trace glauconite grains, minor very fine carbonaceous specks, rare nodular pyrite, rare light brown LIMESTONE fragments, trace micro-micaceous, soft to moderately hard, sub-blocky to blocky, trace sub fissile. |
| 1900 | 1905 | 100 | SILTSTONE: medium grey brown, medium grey, dark brown, argillaceous, trace arenaceous, trace glauconite grains, minor very fine carbonaceous specks, rare nodular pyrite, trace micro-micaceous, soft to moderately hard, sub-blocky to blocky, trace sub fissile. |
| 1905 | 1910 | 90 10 | SILTSTONE: medium grey brown, pale brown, medium grey, argillaceous, trace arenaceous, trace glauconite grains, minor very fine carbonaceous specks, trace light brown LIMESTONE fragments, trace micro-micaceous, rare pyrite nodules, soft to firm, minor dispersive and amorphous, sub-blocky to blocky. SANDSTONE: off white, clear to translucent, very fine to fine grained, trace medium grained, moderately well sorted, sub-angular to sub-rounded, trace calcareous cement, trace off white argillaceous matrix, generally loose clean grains, minor friable, poor visual and inferred porosity, no fluorescence. |
| 1910 | 1915 | 100 | SILTSTONE: grey brown, medium grey, argillaceous, trace arenaceous, rare glauconite grains, trace very fine carbonaceous specks, rare nodular pyrite, trace micro-micaceous, trace brown LIMESTONE fragments, soft to moderately hard, sub-blocky to blocky. |
| 1915 | 1920 | 100 | SILTSTONE: grey brown, medium grey, argillaceous, trace arenaceous, rare glauconite grains, trace very fine carbonaceous specks, rare nodular pyrite, trace micro-micaceous, trace brown LIMESTONE fragments, soft to moderately hard, sub-blocky to blocky. |
| 1920 | 1925 | 100 | SILTSTONE: grey brown, medium grey, argillaceous, trace arenaceous, rare glauconite grains, trace very fine carbonaceous specks, rare nodular pyrite, trace micro-micaceous, minor LIMESTONE fragments, soft to moderately hard, sub-blocky to blocky. LIMESTONE: (Trace) light brown, buff brown, argillaceous, micritic, rare pyrite inclusion, hard to brittle, sub blocky. |
| 1925 | 1930 | 100 | SILTSTONE: medium brown grey, medium grey, argillaceous, rare glauconite grains, trace very fine carbonaceous specks, rare nodular pyrite, trace micro-micaceous, trace brown LIMESTONE fragments, soft to moderately hard, sub-blocky to blocky. |
| 1930 | 1935 | 100 | SILTSTONE: medium brown grey, medium grey, argillaceous, rare glauconite grains, trace very fine carbonaceous specks, rare nodular pyrite, trace micro-micaceous, trace brown LIMESTONE fragments, soft to moderately hard, sub-blocky to blocky. |
| 1935 | 1940 | 100 | SILTSTONE: medium brown grey, medium grey, argillaceous, rare glauconite grains, rare very fine carbonaceous specks, rare nodular pyrite, trace LIMESTONE fragments, soft to moderately hard, sub-blocky to blocky. |
| 1940 | 1945 | 100 | SILTSTONE: medium brown grey, medium grey, argillaceous, rare glauconite grains, rare very fine carbonaceous specks, rare nodular pyrite, trace LIMESTONE fragments, soft to moderately hard, sub-blocky to blocky. |
| 1945 | 1950 | 100 | SILTSTONE: medium brown grey, medium grey, argillaceous, rare glauconite grains, rare very fine carbonaceous specks, rare nodular pyrite, trace LIMESTONE fragments, soft to moderately hard, sub-blocky to blocky. |
| 1950 | 1955 | 100 | SILTSTONE: medium brown grey, medium grey, argillaceous, rare glauconite grains, rare very fine carbonaceous specks, rare nodular pyrite, trace micritic & micro-crystalline LIMESTONE fragments, soft to moderately hard, sub-blocky to blocky. |
| 1955 | 1960 | 100 | SILTSTONE: medium brown grey, medium grey, argillaceous, rare glauconite grains, rare very fine carbonaceous specks, rare nodular pyrite, trace micritic & micro-crystalline LIMESTONE fragments, soft to moderately hard, sub-blocky to blocky. |
| 1960 | 1965 | 100 | SILTSTONE: medium brown grey, medium grey, argillaceous, trace to minor glauconite grains, rare very fine carbonaceous specks, rare nodular & banded pyrite, trace micritic & micro-crystalline LIMESTONE fragments, firm to moderately hard, trace soft, sub-blocky to blocky. |
| 1965 | 1970 | 95 5 | SILTSTONE: medium grey brown, pale brown, medium grey, argillaceous, trace arenaceous, common glauconite grains, minor very fine carbonaceous specks, trace light brown LIMESTONE fragments, trace micro-micaceous, rare pyrite nodules, soft to firm, minor dispersive and amorphous, sub-blocky to blocky. SANDSTONE: clear to translucent, very fine to fine grained, moderately well sorted, sub-angular to sub-rounded, generally loose clean grains, poor visual and inferred porosity, no fluorescence. |
| 1970 | 1975 | 90 10 | SILTSTONE: grey brown, pale brown, medium grey, argillaceous, trace arenaceous, common glauconite grains, minor very fine carbonaceous specks, trace light brown LIMESTONE fragments, trace micro-micaceous, trace pyrite bands, soft to firm, trace moderately hard, sub-blocky to blocky. SANDSTONE: clear to translucent, very fine to fine grained, trace medium grained, moderately well sorted, sub-angular to sub-rounded, generally loose clean grains, poor visual and inferred porosity, no fluorescence. |
| 1975 | 1980 | 95 5 | SILTSTONE: grey brown, pale brown, medium grey, argillaceous, trace arenaceous, abundant glauconite grains, minor very fine carbonaceous specks, trace light brown LIMESTONE fragments, trace micro-micaceous, trace pyrite bands, soft to firm, trace moderately hard, sub-blocky to blocky. SANDSTONE: clear to translucent, very fine to fine grained, trace medium grained, moderately well sorted, sub-angular to rounded, glauconitic in part, generally loose clean grains, poor visual and inferred porosity, no fluorescence. |
| 1980 | 1985 | 100 Trace | SILTSTONE: grey brown, pale brown, medium grey, argillaceous, trace arenaceous, abundant glauconite grains, minor very fine carbonaceous specks, trace light brown LIMESTONE fragments, trace micro-micaceous, trace pyrite nodules, soft to moderately hard, sub-blocky to blocky. SANDSTONE: clear to translucent, very fine to fine grained, trace medium grained, moderately well sorted, sub-angular to rounded, glauconitic in part, generally loose clean grains, poor visual and inferred porosity, no fluorescence. |
| 1985 | 1990 | 100 | SILTSTONE: grey brown, light grey, argillaceous, minor arenaceous, abundant glauconite grains, minor very fine carbonaceous specks, trace micro-micaceous, trace pyrite nodules, trace quartz grains, soft to moderately hard, sub-blocky to blocky. |
| 1990 | 1995 | 90 10 | SILTSTONE: grey brown, pale brown, medium grey, argillaceous, trace arenaceous, abundant glauconite grains, minor very fine carbonaceous specks, trace light brown LIMESTONE fragments, trace micro-micaceous, trace pyrite nodules, soft to moderately hard, sub-blocky to blocky. SANDSTONE: clear to translucent, very fine to fine grained, well sorted, sub-angular to rounded, trace glauconite, generally clean loose grains, poor visual and inferred porosity, no fluorescence. |
| 1995 | 1998 | 100 | SILTSTONE: light to medium grey brown, medium grey, argillaceous, trace arenaceous, common glauconite grains, minor very fine carbonaceous specks, trace light brown LIMESTONE fragments, trace micro-micaceous, rare pyrite nodules, soft to moderately hard, sub-blocky to blocky. |
| 1998 | 2000 | 100 | SILTSTONE: medium grey brown, medium grey, argillaceous, trace arenaceous, common glauconite grains, minor very fine carbonaceous specks, trace light brown LIMESTONE fragments, trace micro-micaceous, rare pyrite nodules, soft to moderately hard, sub-blocky to blocky. |
| 2000 | 2005 | 100 | SILTSTONE: medium grey brown, medium grey, argillaceous, trace arenaceous, common glauconite grains, minor very fine carbonaceous specks, trace light brown LIMESTONE fragments, trace micro-micaceous, rare pyrite nodules, firm to moderately hard, sub-blocky to blocky. |
| 2005 | 2010 | 100 | SILTSTONE: medium grey brown, medium grey, occasionally pale grey, argillaceous, trace arenaceous, common glauconite grains, minor very fine carbonaceous specks, trace light brown LIMESTONE fragments, trace micro-micaceous, rare pyrite nodules, firm to moderately hard, sub-blocky to blocky. |
| 2010 | 2015 | 100 | SILTSTONE: medium grey brown, medium to dark grey, occasionally pale grey, argillaceous, trace arenaceous, common glauconite grains, minor very fine carbonaceous specks, trace light brown LIMESTONE fragments, rare pyrite nodules, firm to moderately hard, sub-blocky to blocky. |
| 2015 | 2020 | 100 | SILTSTONE: medium grey brown, medium to dark grey, occasionally pale grey, argillaceous, trace arenaceous, common glauconite grains, minor very fine carbonaceous specks, trace light brown LIMESTONE fragments, rare pyrite nodules, firm to moderately hard, sub-blocky to blocky, minor sub-fissile. |
| 2020 | 2025 | 100 | SILTSTONE: medium grey brown, medium to dark grey, argillaceous, trace arenaceous, common glauconite grains, minor carbonaceous specks, trace light brown LIMESTONE fragments, rare pyrite nodules, firm to moderately hard, sub-blocky to blocky, minor sub-fissile. |
| 2025 | 2028 | 100 | SILTSTONE: medium grey brown, medium to dark grey in part, argillaceous, rare arenaceous, common glauconite grains, minor carbonaceous specks, trace light brown LIMESTONE fragments, rare pyrite nodules, firm to moderately hard, sub-blocky to blocky, minor sub-fissile. |
| 2028 | 2031 | 100 | SILTSTONE: medium grey brown, medium to dark grey in part, argillaceous, rare arenaceous, common glauconite grains, minor carbonaceous specks, trace light brown LIMESTONE fragments, rare pyrite nodules, firm to dominantly moderately hard, sub-blocky to blocky, minor sub-fissile. |
| 2031 | 2034 | 100 | SILTSTONE: medium brown to grey brown, medium to dark grey in part, argillaceous, rare arenaceous, common glauconite grains, minor carbonaceous specks, occasional calcareous inclusions, rare pyrite nodules, firm to dominantly moderately hard, sub-blocky to blocky, minor sub-fissile. |
| 2034 | 2037 | 100 | SILTSTONE: medium brown to grey brown, pale to medium grey in part, argillaceous, rare arenaceous, common glauconite grains, minor carbonaceous specks, occasional calcareous inclusions, rare pyrite nodules, firm to dominantly moderately hard, sub-blocky to blocky, minor sub-fissile. |
| 2037 | 2039 | 100 | SILTSTONE: medium brown to grey brown, pale to medium grey in part, argillaceous, rare arenaceous, common glauconite grains, minor carbonaceous specks, occasional calcareous inclusions, rare pyrite nodules, firm to dominantly moderately hard, sub-blocky to blocky, minor sub-fissile. |
| 2039 | 2042 | 80 20 | SILTSTONE: medium brown, pale to medium grey in part, argillaceous, rare arenaceous, common glauconite grains, minor carbonaceous specks, occasional calcareous inclusions, rare pyrite nodules, firm to dominantly moderately hard, sub-blocky to blocky, minor sub-fissile. SANDSTONE: pale grey to grey brown, very fine, well sorted, sub-angular to sub-round, weak to moderately siliceous cement, common to abundant pale brown silty matrix, occasional glauconite grains and carbonaceous specks, friable, very poor visual porosity, no fluorescence. |
| 2042 | 2045 | 70 30 | SILTSTONE: pale to medium brown, pale to medium grey in part, argillaceous, rare arenaceous, common glauconite grains, minor carbonaceous specks, occasional calcareous inclusions, rare pyrite nodules, firm to dominantly moderately hard, sub-blocky to minor sub-fissile. SANDSTONE: pale grey to grey brown, off white, very fine, well sorted, sub-angular to sub-round, weak to moderately siliceous cement, common to abundant pale brown to off white silty matrix, occasional glauconite grains and carbonaceous specks, friable, very poor visual porosity, no fluorescence. |
| 2045 | 2047 | 40 60 | SILTSTONE: pale to medium brown, pale to medium grey in part, argillaceous, rare arenaceous, common glauconite grains, minor carbonaceous specks, occasional calcareous inclusions, rare pyrite nodules, firm to dominantly moderately hard, sub-blocky to minor sub-fissile. SANDSTONE: pale grey to grey brown, off white, very fine, well sorted, sub-angular to sub-round, weak to moderately siliceous cement, common to abundant pale brown to off white silty matrix, occasional glauconite grains and carbonaceous specks, minor pyrite nodules, friable, very poor visual porosity, no fluorescence. |