LAKES OIL N.L. A.C.N. (004 247 214) LOY YANG No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 10 Date: 14-03-2006

Depth: 1164m Progress: 121m Days from Spud: 10

Rig: HUNT RIG No.2 GL(AHD): 104.00m Drilling Rep: Lou DeVattimo RT: (datum) 107.65m Geologist: David Horner Last Casing: 178mm at 220m

0600 hrs Update: RIH with new bit drill ahead with 156mm hole to 1185m. Lithology: interbedded and laminated sandstone/claystone and minor coal. Maximum gas 84 units from coal at 1177m.

Comments: Drill ahead with 156mm hole to 1164m, POOH for new bit.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1043-1164 | Strzelecki Formation Maximum gas readings 50 units from coal at 1074m. CUT: The coal has no fluorescence but give a weak dull milky white crush cut. FLUORESCENCE: The sandstones from 1152m have very dull patchy orange residual oil fluorescence, no discernable cut. | TG 1-50u C1 100% C2+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Haunted Hills Gravels LaTrobe Group Carrajung Volcanics | 3.7 23.45 130.45 | 3.7 n/p n/p | 3.7 n/p n/p | 0 - - |
| Strzelecki Formation | 148.45 | n/p | n/p | - |
| T.D. | 1000 |  |  |  |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) LOY YANG No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 10

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1043-1164 | STRZELECKI FORMATION Sandstone (50%) interbedded and laminated with Claystone (50%) and minor laminated Coal (Trace). SANDSTONE: off white to medium green grey, very fine to fine, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant light green grey argillaceous matrix, abundant altered feldspar grains, common grey green lithics, trace quartz grains, trace orange brown and black lithics, abundant black coal detritus, trace calcite veining, hard, no visual porosity, no oil fluorescence. CLAYSTONE: medium to dark grey to medium brown grey, often very silty, very finely arenaceous with altered feldspars grains in part, slightly to very carbonaceous, abundant black coal detritus, trace micromica, trace calcite veining, moderately hard, subfissile. COAL: black, platy to subconchoidal fracture, striated in part, subvitreous where clean, earthy and argillaceous in part, cleated, hard, brittle. CUT: The coal has no fluorescence but give a weak dull milky white crush cut. FLUORESCENCE: The sandstones from 1152m have very dull patchy orange residual oil fluorescence, no discernable cut. |