LAKES OIL N.L. A.C.N. (004 247 214) LOY YANG No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 2 Date: 06-03-2006

Depth: 231m Progress: 11m Days from Spud: 2

Rig: HUNT RIG No.2 GL(AHD): 104.00m Drilling Rep: Lou DeVattimo RT: (datum) 107.65m Geologist: David Horner Last Casing: 178mm at 220m

0600 hrs Update: Drill ahead with 156mm hole at 307m. Lithology 70% argillaceous very fine tight Sandstone laminated with and grading to 30% very finely arenaceous Claystone. Background gas 0.7 to 3.3 units (C1 100%).

Comments: Nipple up and pressure test BOP's, drillout shoe track and new 156mm hole to 223m, perform FIT to 200 PSI with 8.4 lb/gal mud - no leak off, EMW of 14.0 lb/gal. Drill ahead with 156mm hole to 231m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 220-231 | Strzelecki Formation | TG 0.7u C1 100% C2 Trace C3+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Haunted Hills Gravels LaTrobe Group Carrajung Volcanics | 3.7 23.45 130.45 | 3.7 n/p n/p | 3.7 n/p n/p | 0 - - |
| Strzelecki Formation | 148.45 | n/p | n/p | - |
| T.D. | 1000 |  |  |  |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) LOY YANG No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 2

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 220-231 | STRZELECKI FORMATION Sandstone (60%) interbedded and laminated with Claystone (40%). SANDSTONE: off white to meium green grey, very fine to occasionally medium, dominantly fine, subangular to subrounded, moderately sorted, moderate silica and calcareous cements, trace dolomite cement, abundant white argillaceous matrix, abundant altered feldspar grains, common grey green lithics, trace quartz grains, rare orange brown and black lithics, trace black carbonaceous detritus, trace to common calcite and dolomite lined veins, moderately hard, no visual porosity, no oil fluorescence. CLAYSTONE: off white to medium green grey to dark brown grey, often very silty, very finely arenaceous with altered feldspars grains in part, slightly carbonaceous in part, trace black coal detritus, trace calcite lined fractures, firm, slightly subfissile. |