LAKES OIL N.L. A.C.N. (004 247 214) LOY YANG No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 8 Date: 12-03-2006

Depth: 890m Progress: 8m Days from Spud: 8

Rig: HUNT RIG No.2 GL(AHD): 104.00m Drilling Rep: Lou DeVattimo RT: (datum) 107.65m Geologist: David Horner Last Casing: 178mm at 220m

0600 hrs Update: Drill ahead with 156mm hole at 919m. Lithology has been a messive sandstone 890-917m, with a carbonaceous claystone 917-919+m. No oil fluorescence encountered through this interval.

Comments: RIH and perform DST No.2 (872.45-882.0m), IF 25 mins, ISI 5 mins, FF 240 mins, FSI 60 mins, IF no blow, FF weak to moderate air blow throughout, NGTS, NFTS, contents of test string reverse circulated out, recovered 142.5m of fresh water, BHT 134° F. Water analysis of sample chamber water same as for DST No.1 (PH 7.4, Cl 550 ppm, Hardness 28 ppm, Alkalinity Trace,0.08, Carbonate Trace, BiCarbonate 73 ppm, Potassium Nil, Sulphite Nil). Lay out test tools, make up and RIH 156mm tricone insert drill bit, trip gas 6 units (C1 100%), drill ahead with 156mm hole to 890m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 882-890 | Strzelecki Formation The coaly material has no fluorescence but give a weak dull milky white crush cut. | TG 0.6-2.5u C1 100% C2+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Haunted Hills Gravels LaTrobe Group Carrajung Volcanics | 3.7 23.45 130.45 | 3.7 n/p n/p | 3.7 n/p n/p | 0 - - |
| Strzelecki Formation | 148.45 | n/p | n/p | - |
| T.D. | 1000 |  |  |  |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) LOY YANG No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 8

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 882-890 | STRZELECKI FORMATION Sandstone (100%) occasionally laminated with Claystone (trace). SANDSTONE: off white to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak to moderate calcareous cements, common to abundant light green grey argillaceous matrix, abundant altered feldspar grains, common grey green lithics, trace to common quartz grains, trace orange brown and black lithics, common black coal detritus, trace calcite veining, hard, no visual porosity, no oil fluorescence. CLAYSTONE: medium to occasionally dark grey to medium green grey to medium brown grey, often very silty, very finely arenaceous with altered feldspars grains in part, slightly to moderately carbonaceous, common black coal detritus, rare micromica, trace calcite veining, moderately hard, subfissile. CUT: The coal has no fluorescence but give a weak dull milky white crush cut. |