LAKES OIL N.L. A.C.N. (004 247 214) LOY YANG No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 9 Date: 13-03-2006

Depth: 1043m Progress: 153m Days from Spud: 9

Rig: HUNT RIG No.2 GL(AHD): 104.00m Drilling Rep: Lou DeVattimo RT: (datum) 107.65m Geologist: David Horner Last Casing: 178mm at 220m

0600 hrs Update: Drill ahead with 156mm hole at 1075m. Current Lithology, interbedded sandstone (40%) with claystone (50%) and coal (10%). Gas from coal 30 units (C1 100%).

Comments: Drill ahead with 156mm hole to 1043m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 890-962 | Strzelecki Formation Maximum gas readings 10.5 units from carbonaceous/coaly material. CUT: The coal has no fluorescence but give a weak dull milky white crush cut. | TG 1-10.5u C1 100% C2+ 0 |
| 962-1043 | Strzelecki Formation Maximum gas readings 33 and 46 units from coaly material. CUT: The coal has no fluorescence but give a weak dull milky white crush cut. | TG 5-46u C1 100% C2+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Haunted Hills Gravels LaTrobe Group Carrajung Volcanics | 3.7 23.45 130.45 | 3.7 n/p n/p | 3.7 n/p n/p | 0 - - |
| Strzelecki Formation | 148.45 | n/p | n/p | - |
| T.D. | 1000 |  |  |  |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) LOY YANG No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 9

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 890-962 | STRZELECKI FORMATION Sandstone (80%) thinly interbedded and laminated with Claystone (20%). SANDSTONE: off white to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, common to abundant light green grey argillaceous matrix, abundant altered feldspar grains, common grey green lithics, common quartz grains, trace orange brown and black lithics, common black coal detritus, trace calcite veining, hard, no visual porosity, no oil fluorescence. CLAYSTONE: medium to occasionally dark grey to medium green grey to medium brown grey, often very silty, very finely arenaceous with altered feldspars grains in part, moderately carbonaceous, common black coal detritus, rare micromica, trace calcite veining, moderately hard, subfissile. CUT: The coal has no fluorescence but give a weak dull milky white crush cut. |
| 962-1043 | STRZELECKI FORMATION Claystone (50%) interbedded and laminated with Sandstone (50%) and minor laminated Coal (Trace). CLAYSTONE: medium to dark grey to medium green grey to medium brown grey, often very silty, very finely arenaceous with altered feldspars grains in part, slightly to moderately carbonaceous, common black coal detritus, rare micromica, trace calcite veining, moderately hard, subfissile. SANDSTONE: off white to medium green grey, very fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant light green grey argillaceous matrix, abundant altered feldspar grains, common grey green lithics, trace quartz grains, trace orange brown and black lithics, common black coal detritus, trace calcite veining, hard, no visual porosity, no oil fluorescence. COAL: black, blocky to striated to subconchoidal fracture, subvitreous where clean, often earthy and very argillaceous, hard, brittle. CUT: The coal has no fluorescence but give a weak dull milky white crush cut. |