LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Loy Yang-2 | REPORT No. : | 10 | DFS: | 9.25 | DATE : | 14-03-2006 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1164 | LAST DEPTH : | 1043 | 24 HR PROGRESS: | 121 | PTD : | 1250m |
| TOTAL FUEL : | 4,100 | FUEL USAGE : | 1,700 | DAYCOST : $ | 30,457 | CUM. COST : $ | 999,088 |
| 0600 OPS : | Drilling 156mm hole at 1185m |
| Next 24 Hrs Op | Drill to TD |
| Site Personnel: | Lakes 4 Higgins 2 Hunt Energy 15 Hunt Camp 4 Aust DST 2 Baroid 1 Total 28 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Run Number | 6 Re-run # 1 | 5 Bit # 2 |  | Drilling | 18.00 |  | Density | 8.60 | PPG |
| Size (mm) | 156 | 156 |  | Tripping | 4.00 |  | Viscosity | 33 | Sec |
| Make | Reed | Reed |  | Surveys | 0.50 |  | Water Loss | 8.2 | Cc |
| Type | DSX416S-A1 | SL43HKPR |  | Rig repairs |  |  | pH | 9.0 | Strip |
| IADC Code |  | 4-3-7 |  | Testing/tools |  |  | Filter Cake | 1.0 | 32 nd |
| Serial Number | 211343 | CD-8051 |  | Circulate Sample |  |  | PV / YP | 3 / 6 | Cp/lb/100’ |
| Nozzles (32) | 12-12-12-12 | 12-12-12 |  | Light reaming |  |  | Gels | 2 / 3 / 4 | S/m |
| Depth in (m) | 1164 | 882 |  | Cementing |  |  | Sand | 0.10 | % Vol |
| Depth out (m) |  | 1164 |  | Slip and Cut line | 0.50 |  | Solids | 1.4 | % Vol |
| Total Metres |  | 282 |  | Circulate & Condition | 0.50 |  | Oil |  | % Vol |
| Hours |  | 42.5 |  | Rig Service | 0.50 |  | K+ |  | Mg/l |
| WOB (kg) |  | 4000 |  | Rig up BOP |  |  | Chlorides | 5,500 | Mg/l |
| RPM |  | 120 |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition |  | 2-2-ER-A-E-I-NO-PR |  | DST |  |  | KCL | 1.10 | % by vol |
| Impact Force |  | 274 |  | Wait On Cement |  |  | Daily Cost $ | 2,499 |
| Jet Velocity |  | 244 |  | Test BOPs |  |  | Cum Cost $ | 29,040 |
| BHA: | Bit –bit sub-2 drill collars-stab- 10 drill collars-jars- 2 drill collars |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From |  | Operation |  | 8 + | ° at | 1157 | m |  | Type | Amount |
| 00:00 | 10:00 | Drilled 156mm hole from 1043m to 1109m |  |  | ° at |  | m |  |  |  |
| 10:00 | 10:30 | Serviced rig |  |  | ° at |  | m |  | Dextrid LTE | 3 |
| 10:30 | 18:30 | Drilled 156mm hole from 1109m to 1164m |  |  | ° at |  | m |  | Baracide |  |
| 18:30 | 19:00 | Circulated |  |  | ° at |  | m |  | N-VIS Plus | 18 |
| 19:00 | 19:30 | Ran survey |  |  | ° at |  | m |  | KCL Tech | 18 |
| 19:30 | 22: 00 | Tripped out for bit change ( slow drill rate ) |  |  | ° at |  | m |  | Baracor 129 | 2 |
| 22:00 | 23:30 | Changed Bit then tripped in hole to shoe |  |  | ° at |  | m |  | Potassium Hydrox | 3 |
| 23:30 | 24:00 | Slipped and cut block line |  |  |  |  |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  |  |  | Liner | 140 | mm |  | Liner |  | mm |
|  |  |  |  | Pressure | 7,700 | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP | 64.8 | f/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC | 100.4 | f/in |  | A.V. DC |  | m/min |
|  |  |  |  | SPM | 45 |  | SPM |  |
|  |  |  |  | GPM | 252 |  | GPM |  |
|  |  | String wt up 60k |  |  |  |  |
|  |  | 54k |  | CEMENT DATA |  | LAST CASING |
|  |  | Down 48k |  | Sacks Halliburton | 198 |  | Size | 177.80 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 38.69 | Kg/m |
|  |  | Held BOP Drill with crew |  | % |  |  |  | Grade | N-80 |  |
|  |  | JSA Tool box meeting F.E.L operations |  | % |  |  |  | Connection | Buttress |  |
|  |  | JSA Working on Mud pump |  | % |  |  |  | Joints | 18 |  |
|  |  |  |  | % |  |  |  | Length | 216.00 | m |
| Days since | LTA | 564 |  | Halliburton cost | $ 31,212 |  | Shoe | 220m from RKB | m |

,66