LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Loy Yang-2 | REPORT No. : | 15 | DFS: | 14.25 | DATE : | 19-03-2006 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1443m | LAST DEPTH : | 1443m | 24 HR PROGRESS: | 0m | PTD : | 1443m |
| TOTAL FUEL : | 6,400 | FUEL USAGE : | 600 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Ran 116jnts 4-1/2” Casing to 1443m- Rig up to circulate prior to cement job |
| Next 24 Hrs Op | Cement casing- Install Casing slips and land same in Wellhead-Run CBL log-Remove BOP-Install Tree-Test same-Release Rig |
| Site Personnel: | Lakes 1 Higgins 2 Hunt Energy 15 Hunt Camp 4 Aust DST 2 Total 24 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Run Number |  |  |  | Drilling |  |  | Density | 8.75 | PPG |
| Size (mm) |  |  |  | Tripping |  |  | Viscosity | 35 | Sec |
| Make |  |  |  | Surveys |  |  | Water Loss | 6.5 | Cc |
| Type |  |  |  | Rig repairs |  |  | pH | 9.00 | Strip |
| IADC Code |  |  |  | Testing/tools |  |  | Filter Cake | 1.0 | 32 nd |
| Serial Number |  |  |  | Circulate Sample |  |  | PV / YP | 6 / 13 | Cp/lb/100’ |
| Nozzles (32) |  |  |  | Light reaming |  |  | Gels | 3 / 4 / 5 | S/m |
| Depth in (m) |  |  |  | Cementing |  |  | Sand | 0.15 | % Vol |
| Depth out (m) |  |  |  | Slip and Cut line |  |  | Solids | 2.7 | % Vol |
| Total Metres |  |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours |  |  |  | Rig service |  |  | K+ |  | Mg/l |
| WOB (kg) |  |  |  | Rig up BOP |  |  | Chlorides | 5,500 | Mg/l |
| RPM |  |  |  | Logging |  |  | PHPA |  |  |
| Condition |  |  |  | DST |  |  | KCL | 1.10 | % by vol |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ | 2,443 |
| Jet Velocity |  |  |  | Test BOPs |  |  | Cum Cost $ | 35,759 |
| BHA: |  |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From |  | Operation |  |  | ° at |  | m |  | Type | Amount |
| 00:00 | 05:30 | Continued DST # 3 |  |  | ° at |  | m |  | Barazan-D plus |  |
| 05:30 | 06:30 | Shut in well for pressure build up |  |  | ° at |  | m |  | Dextrid LTE |  |
| 06:30 | 08:30 | Unseated Packer then reversed out fluid in pipe ( water) |  |  | ° at |  | m |  | Baracide / Pac-L |  |
| 08:30 | 16:00 | Pulled out laying out the pipe string |  |  | ° at |  | m |  | N-VIS Plus |  |
| 16:00 | 16:30 | Picked up Kelly and broke out crossover connections |  |  | ° at |  | m |  | KCL Tech |  |
| 16:30 | 17:00 | Layed out remainder of pipe |  |  | ° at |  | m |  | Baracor 129 |  |
| 17:00 | 19:30 | Layed out DST tools recovered gauges -water sample |  |  | ° at |  | m |  | Potassium Hydrox |  |
| 19:30 | 20:00 | Layed out drill collars |  |  |  |  |
| 20:00 | 22:00 | Layed out Kelly and Kelly spinner |  | PUMP 1 |  | PUMP 2 |
| 22:00 | 23:00 | Rigged up for running Casing |  | Liner | 140 | mm |  | Liner |  | mm |
| 23:00 | 24:00 | Held safety meeting then ran 4-1/2” Casing |  | Pressure | 7,700 | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP | 64.8 | f/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC | 100.4 | f/in |  | A.V. DC |  | m/min |
|  |  |  |  | SPM | 45 |  | SPM |  |
|  |  |  |  | GPM | 252 |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  | DST invoice $ 31,300 |  | Sacks Halliburton | 198 |  | Size | 177.80 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 38.69 | Kg/m |
|  |  |  |  | % |  |  |  | Grade | N-80 |  |
|  |  | JSA Laying out pipe |  | % |  |  |  | Connection | Buttress |  |
|  |  | JSA |  | % |  |  |  | Joints | 18 |  |
|  |  |  |  | % |  |  |  | Length | 216.00 | m |
| Days since | LTA | 568 |  | Halliburton cost | $ 31,212 |  | Shoe | 220m from RKB | m |

,66