LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Loyang-2 | REPORT No. : | 6 | DFS: | 5.25 | DATE : | 10-03-2006 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 690.00m | LAST DEPTH : | 458.00 | 24 HR PROGRESS: | 232.00m | PTD : | 1250m |
| TOTAL FUEL : | 6,900 | FUEL USAGE : | 1,200 | DAYCOST : $ | 57,740 | CUM. COST : $ | 855,035 |
| 0600 OPS : | Drilling 156mm hole at 795 m |
| Next 24 Hrs Op | Drill ahead |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 4 RR-1 |  |  | Drilling | 17.50 |  | Density | 8.7 | PPG |
| Size (mm) | 156 |  |  | Tripping | 4.00 |  | Viscosity | 41 | Sec |
| Make | Reed |  |  | Surveys | 0.50 |  | Water Loss | 6.8 | Cc |
| Type | DSX |  |  | Rig repairs |  |  | pH | 8.8 | Strip |
| IADC Code | S-222 |  |  | Testing/tools |  |  | Filter Cake | 1.00 | 32 nd |
| Serial Number | 211343 |  |  | Circulate Sample |  |  | PV / YP | 6 / 14 | Cp/lb/100’ |
| Nozzles (32) | 12-12-12-12 |  |  | Light reaming | 0.50 |  | Gels | 4 / 5 / 6 | S/m |
| Depth in (m) | 458 |  |  | Cementing |  |  | Sand | 0.10 | % Vol |
| Depth out (m) |  |  |  | Coring |  |  | Solids | 2.1 | % Vol |
| Total Metres | Drilled so far 455m |  |  | Circulate & Condition | 1.00 |  | Oil |  | % Vol |
| Hours | 40 |  |  | Rig Service | 0.50 |  | K+ |  | Mg/l |
| WOB (kg) | 3000 |  |  | Rig up BOP |  |  | Chlorides | 6,500 | Mg/l |
| RPM | 120 |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition | in |  |  | DST |  |  | KCL | 1.30% by volume |  |
| Impact Force | 207lbft |  |  | Wait On Cement |  |  | Daily Cost $ | 2,923 |
| Jet Velocity | 183ft/sec |  |  | Test BOPs |  |  | Cum Cost $ | 19,966 |
| BHA: |  |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From |  | Operation |  | 2.00 | ° at | 650 | m |  | Type | Amount |
| 0000 | 02;30 | Made up 156mm Bit then tripped in hole to 440m |  |  | ° at |  | m |  |  |  |
| 02:30 |  | Washed from 440m to 450m then light reamed core |  |  | ° at |  | m |  | Dextrid LTE | 4 |
|  | 03:00 | Rathole from 450m to 458m |  |  | ° at |  | m |  | Baracide | 1 |
| 03:00 | 10:00 | Drilled 156mm hole from 458m to 546m |  |  | ° at |  | m |  | N-VIS Plus | 20 |
| 10;00 | 10;30 | Serviced the rig |  |  | ° at |  | m |  | KCL Tech | 26 |
| 10:30 | 20:00 | Drilled 156mm hole from 546m to 652m |  |  | ° at |  | m |  | Baracor 129 | 1 |
| 20;00 | 20;30 | Circulated hole clean ran survey on wireline |  |  | ° at |  | m |  | Potassium Hydrox | 1 |
| 20;30 | 21:30 | Wiper tripped 10 stands hole good ( 470m ) |  |  |  |  |
| 21;30 | 22:00 | Picked up Kelly washed from 643m to 652 no fill |  | PUMP 1 |  | PUMP 2 |
| 22;00 | 24:00 | Drilled 156mm hole from 652m to 690m |  | Liner | 140 | mm |  | Liner |  | mm |
|  |  |  |  | Pressure | 4,900 | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP | 64.8 | f/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC | 100.4 | f/in |  | A.V. DC |  | m/min |
|  |  |  |  | SPM | 45 |  | SPM |  |
|  |  |  |  | GPM | 252 |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton | 198 |  | Size | 177.80 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 38.69 | Kg/m |
|  |  |  |  | % |  |  |  | Grade | N-80 |  |
|  |  | JSA Held safety meeting on tripping with drill collars |  | % |  |  |  | Connection | Buttress |  |
|  |  | JSA Laying down drill pipe from mousehole |  | % |  |  |  | Joints | 18 |  |
|  |  |  |  | % |  |  |  | Length | 216.00 | m |
| Days since | LTA | 561 |  | Halliburton cost | $ 31,212 |  | Shoe | 220m from RKB | m |

,66