LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Loy Yang-2 | REPORT No. : | 7 | DFS: | 6.25 | DATE : | 11-03-2006 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 882.00m | LAST DEPTH : | 690.00 | 24 HR PROGRESS: | 192.00m | PTD : | 1250m |
| TOTAL FUEL : | 8,750 | FUEL USAGE : | 1,880 | DAYCOST : $ | 28,349 | CUM. COST : $ | 883,384 |
| 0600 OPS : | Opened tool for Drill stem test # 2 Packer set at 872m |
| Next 24 Hrs Op | Test then drill ahead |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 4 RR-1 |  |  | Drilling | 15.00 |  | Density | 8.65 | PPG |
| Size (mm) | 156 |  |  | Tripping | 5.00 |  | Viscosity | 37 | Sec |
| Make | Reed |  |  | Surveys | 3.50 |  | Water Loss | 7.5 | Cc |
| Type | DSX |  |  | Rig repairs |  |  | pH | 9.50 | Strip |
| IADC Code | S-222 |  |  | Testing/tools |  |  | Filter Cake | 1.0 | 32 nd |
| Serial Number | 211343 |  |  | Circulate Sample |  |  | PV / YP | 5 / 10 | Cp/lb/100’ |
| Nozzles (32) | 12-12-12-12 |  |  | Light reaming |  |  | Gels | 3 / 4 / 5 | S/m |
| Depth in (m) | 458 |  |  | Cementing |  |  | Sand | 0.10 | % Vol |
| Depth out (m) | 882 |  |  | Coring |  |  | Solids | 1.8 | % Vol |
| Total Metres | 643 |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours | 49 |  |  | Rig Service | 0.50 |  | K+ |  | Mg/l |
| WOB (kg) | 3000 |  |  | Rig up BOP |  |  | Chlorides | 7,000 | Mg/l |
| RPM | 120 |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition |  |  |  | DST |  |  | KCL | 1.40 | % by vol |
| Impact Force | 207lbft |  |  | Wait On Cement |  |  | Daily Cost $ | 2,892 |
| Jet Velocity | 183ft/sec |  |  | Test BOPs |  |  | Cum Cost $ | 22,858 |
| BHA: | Bit –bit sub-2 drill collars-stab- 10 drill collars-jars- 2 drill collars |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From |  | Operation |  | 4.5 + | ° at | 632 | m |  | Type | Amount |
| 0000 | 09:30 | Drilled 156mm hole from 690m to 853m |  | 8.0 + | ° at | 708 | m |  |  |  |
| 09:30 | 10:00 | Serviced the rig |  | 8.0 + | ° at | 736 | m |  |  |  |
| 10:00 | 10:30 | Ran survey at 842m |  | 8.0 + | ° at | 842 | m |  |  |  |
| 10:30 | 11:30 | Wiper tripped to 660m hole good |  | 8.0 + | ° at | 853 | m |  | N-VIS Plus | 26 |
| 11:30 | 12:00 | Ran survey at 842m |  | 8.0 + | ° at | 882 | m |  | KCL Tech | 35 |
| 12:00 | 13:00 | Drilled 156mm hole from 853m to 863m |  |  | ° at |  | m |  | Baracor 129 | 2 |
| 13:00 | 13:30 | Ran survey at 853m |  |  | ° at |  | m |  | Potassium Hydrox | 2 |
| 13:30 | 14:00 | Pulled back to 736m |  |  |  |  |
| 14:00 | 14:30 | Ran survey at 736m |  | PUMP 1 |  | PUMP 2 |
| 14:30 | 15:00 | Pulled back to 632m |  | Liner | 140 | mm |  | Liner |  | mm |
| 15:00 | 15:30 | Ran survey at 632m |  | Pressure | 4,900 | kPa |  | Pressure |  | KPa |
| 15:30 | 16:00 | Ran back in hole to 708m |  | A.V. DP | 64.8 | f/min |  | A.V. DP |  | m/min |
| 16:00 | 16:30 | Ran survey at 708m |  | A.V. DC | 100.4 | f/in |  | A.V. DC |  | m/min |
| 16:30 | 17:00 | Ran back in hole to 863m |  | SPM | 45 |  | SPM |  |
| 17:00 | 21:30 | Drilled 156mm hole from 863m to 882m |  | GPM | 252 |  | GPM |  |
| 21:30 | 22:00 | Circulated bottoms up sample |  |  |  |  |
| 22:00 | 24:00 | Tripped out for Drill Stem Test # 2 |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton | 198 |  | Size | 177.80 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 38.69 | Kg/m |
|  |  |  |  | % |  |  |  | Grade | N-80 |  |
|  |  | JSA Mousehole connections |  | % |  |  |  | Connection | Buttress |  |
|  |  | JSA Surveys |  | % |  |  |  | Joints | 18 |  |
|  |  |  |  | % |  |  |  | Length | 216.00 | m |
| Days since | LTA | 561 |  | Halliburton cost | $ 31,212 |  | Shoe | 220m from RKB | m |

,66