LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Loy Yang-2 | REPORT No. : | 8 | DFS: | 7.25 | DATE : | 12-03-2006 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 890.00m | LAST DEPTH : | 882.00 | 24 HR PROGRESS: | 8.00m | PTD : | 1250m |
| TOTAL FUEL : | 7,050 | FUEL USAGE : | 1,700 | DAYCOST : $ | 35,933 | CUM. COST : $ | 921,817 |
| 0600 OPS : | Drilling 156mm hole at 919m |
| Next 24 Hrs Op | Drill ahead |
| Site Personnel: | Lakes 4 Higgins 2 Hunt Energy 15 Hunt Camp 4 Aust DST 2 Baroid 1 Total 28 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Run Number | 4 RR-1 | 5 Bit # 2 |  | Drilling |  |  | Density | 8.60 | PPG |
| Size (mm) | 156 | 156 |  | Tripping |  |  | Viscosity | 37 | Sec |
| Make | Reed | Reed |  | Surveys |  |  | Water Loss | 7.5 | Cc |
| Type | DSX | SL43HKPR |  | Rig repairs |  |  | pH | 9.50 | Strip |
| IADC Code | S-222 | 4-3-7 |  | Testing/tools |  |  | Filter Cake | 1.0 | 32 nd |
| Serial Number | 211343 | CD-8051 |  | Circulate Sample |  |  | PV / YP | 5 / 8 | Cp/lb/100’ |
| Nozzles (32) | 12-12-12-12 | 12-12-12 |  | Light reaming |  |  | Gels | 3 / 4 / 5 | S/m |
| Depth in (m) | 458 | 882 |  | Cementing |  |  | Sand | 0.10 | % Vol |
| Depth out (m) | 882 |  |  | Coring |  |  | Solids | 1.3 | % Vol |
| Total Metres | 643 | 8 |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours | 49 | 1.00 |  | Rig Service |  |  | K+ |  | Mg/l |
| WOB (kg) | 3000 | 4000 |  | Rig up BOP |  |  | Chlorides | 7,000 | Mg/l |
| RPM | 120 | 120 |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition | As new |  |  | DST |  |  | KCL | 1.40 | % by vol |
| Impact Force | 207lbft | 274 |  | Wait On Cement |  |  | Daily Cost $ | 1,275 |
| Jet Velocity | 183ft/sec | 244 |  | Test BOPs |  |  | Cum Cost $ | 24,133 |
| BHA: | Bit –bit sub-2 drill collars-stab- 10 drill collars-jars- 2 drill collars |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From |  | Operation |  | 4.00 | ° at | 223 | m |  | Type | Amount |
| 0000 | 01:30 | Tripped out for DST # 2 |  | 1.00 | ° at | 450 | m |  |  |  |
| 01:30 | 05:30 | Made up DST tools then tripped in hole |  | 4.50 | ° at | 650 | m |  |  |  |
| 05:30 | 06;00 | Made up and tested surface equipment |  |  | ° at |  | m |  |  |  |
| 06:00 | 11:30 | Performed test |  |  | ° at |  | m |  | N-VIS Plus | 2 |
| 11:30 |  | Unseated packer –dropped bar and reversed out 3.5 |  |  | ° at |  | m |  | KCL Tech |  |
|  | 12:30 | barrel influx of water |  |  | ° at |  | m |  | Baracor 129 | 1 |
| 12;30 | 13:00 | Rigged down surface tools |  |  | ° at |  | m |  | Potassium Hydrox |  |
| 13:00 | 16:00 | Tripped out and layed out tools |  |  |  |  |
| 16:00 | 16:30 | Serviced the rig |  | PUMP 1 |  | PUMP 2 |
| 16:30 | 20;00 | Made up Bit # 2 and BHA tripped in hole to 223m |  | Liner | 140 | mm |  | Liner |  | mm |
| 20:00 | 20:30 | Ran survey at 223m |  | Pressure | 6,300 | kPa |  | Pressure |  | KPa |
| 20:30 | 21:00 | Tripped in hole to 450m |  | A.V. DP | 64.8 | f/min |  | A.V. DP |  | m/min |
| 21:00 | 21:30 | Ran survey at 450m |  | A.V. DC | 100.4 | f/in |  | A.V. DC |  | m/min |
| 21;30 | 22:00 | Tripped in hole to 650m |  | SPM | 45 |  | SPM |  |
| 22:00 | 22:30 | Ran survey at 650m |  | GPM | 252 |  | GPM |  |
| 22:30 | 23:00 | Tripped in hole to bottom at 882m |  |  |  |  |
| 23:00 | 24:00 | Drilled 156mm hole from 882m to 890m |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton | 198 |  | Size | 177.80 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 38.69 | Kg/m |
|  |  |  |  | % |  |  |  | Grade | N-80 |  |
|  |  | JSA Safety meeting prior to Drill stem test |  | % |  |  |  | Connection | Buttress |  |
|  |  | JSA Laying out Jars |  | % |  |  |  | Joints | 18 |  |
|  |  |  |  | % |  |  |  | Length | 216.00 | m |
| Days since | LTA | 562 |  | Halliburton cost | $ 31,212 |  | Shoe | 220m from RKB | m |

,66