Report for :    Robert Spence / Mark Calicutt

Compiled by  :     Colin Chadwick / Dan Dennis

| WELL | SNA-A26A |
| --- | --- |
| DATE | 11-12-2008 |
| REPORT # | 32 |
| MIDNIGHT ACTIVITY | Pump out of hole @ 6227.0 mMDRT |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 6456.0 mMDRT |  | MINIMUM | 5.40 | 6379.0 |
| TVD | 2371.7 mTVDRT |  | MAXIMUM | 69.19 | 6112.0 |
| PROGRESS LAST 24 hrs | 375.0 m |  | AVERAGE | 15.63 |  |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.7m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Lakes Entrance Fm. | 5040.0 | 1377.1 | -1335.4 | 0.9 H | 5052.0 | 1378.0 |
| Top of Latrobe Grp | 5470.0 | 1520.6 | -1478.9 | 1.6 L | 5479.0 | 1519.0 |
| Top Coarse Clastics | 5491.5 | 1534.5 | -1492.8 | 10.5 H | 5518.0 | 1545.0 |
| N-1.4 Coal | 5562.5 | 1588.0 | -1546.3 | 4.0 H | 5576.0 | 1592.0 |
| N-1.9 Coal | 5670.5 | 1678.3 | -1636.6 | 3.7 H | 5682.0 | 1682.0 |
| N-1.9 Reservoir | 5684.3 | 1690.2 | -1648.5 | 2.8 H | 5690.0 | 1693.0 |
| M-2 Upper Reservoir | 5744.8 | 1741.5 | -1699.8 | 3.5H | 5755.0 | 1745.0 |
| M-2 Lower Reservoir | 5771.9 | 1765.0 | -1723.3 | 1.0L | 5776.0 | 1764.0 |
| L-5 Reservoir | 5906.7 | 1884.5 | -1842.8 | 11.5H | 5925.0 | 1896.0 |
| L-8 Reservoir |  |  |  |  | 5985.0 | 1951.0 |
| Top Volcanics | 6043.7 | 2006.0 | -1964.3 | 18.0H | 6069.0 | 2024.0 |
| Base Volcanics | 6060.2 | 2021.0 | -1979.3 | 18.0H | 6088.0 | 2039.0 |
| Sub Volcanic Reservoir | 6074.2 | 2033.0 | -1991.3 | 24.0H | 6100.0 | 2057.0 |
| Top F-1 Sands |  |  |  |  | 6215.0 | 2154.0 |
| Top T-1 Sands | 6359.0 | 2285.5 | -2243.8 | 14.5H | 6380.0 | 2300.0 |
| Base T-1 Sands |  |  |  |  | 6402.0 | 2320.0 |
| Total Depth | 6456.2 | 2371.9 | -2330.2 | 1.1H | 6463.0 | 2373.0 |

| Current Formation |  |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 6088.0 | 885 | 14.9 | 0.3 | 0.07 | 0.02 | 0.004 |  |
| MAX (GFF) | 6104.0 | 414 | 7.9 | 0.2 | 0.05 | 0.01 | 0.004 |  |
| BG (Reserval) |  | 59.2 | 0.8 | 0.06 | 0.02 | 0.008 | 0.002 |  |
| BG (GFF) |  | 19.2 | 0.3 | 0.02 | 0.007 | 0.002 | 0.001 |  |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - |  |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 4 | 3RR |
| SIZE (in) | 9½" | 12¼" |
| MANUFACTURER/TYPE | Reed Hycalog RSR616M-B4 | Reed Hycalog RSR616M-A10 |
| JETS (/32 inch) | 6 x 20 | 6 x 24 |
| DEPTH IN (m) | 5486.0 | 5486.0 |
| DEPTH OUT (m) |  | 5486.0 |
| METRES ON RUN (m) | 970.0 |  |
| HRS ON BTM 24hrs/total | 12.9/31.0 |  |
| BIT CONDITION |  |  |
| RPM RANGE 24hrs | 86-146 |  |
| Pump Hrs 24 hrs / total | 22.1/64.3 |  |
| Krevs 24 hrs / total | 219/567 |  |

| 24 HOUR SUMMARY | Drill and survey 9 ½” hole from 6081.0 mMDRT to 6456.0 mMDRT. Circulate hole clean, staging up pumps to 700 gpm, racking back 1 stand each bottoms up. Pump out of hole. |
| --- | --- |
| 11-12-2008 5AM UPDATE | Continue to pump out of hole. Work overpull at 6052.0 mMDRT. RIH to 6110.0 mMDRT and circulate bottoms up. Pump out of hole, no go at 6052.0 mMDRT. Back ream out of the hole. Continue to pump out of the hole, tight spot at 6044.0 mMDRT. Back ream out of the hole. Pump out of the hole from 6022.0 mMDRT to 5935.0 mMDRT. |