LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 36 Date: 14-11-2005

Depth: 2271m Progress: 0m Days from Spud: 36

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: RIH with 152mm mill tooth bit and junk sub, trip gas 0.5 units, drill ahead with 152mm hole to 2277m. Current Lithology Sandstone (90%) laminated with Claystone (10%), background gas trace.

Comments: POOH at 2271m due to high torque, bit missing one cone, make up and RIH reverse circulation junk basket, work junk basket, POOH, recover lost cone, RIH with 152mm mill tooth bit and junk sub.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
|  | No new formation drilled |  |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 36

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
|  | No new formation drilled. |