LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 10 | DFS: | 10 | DATE : | 26-10-9 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1304 | LAST DEPTH : | 1184 | 24 HR PROGRESS: | 120 | PTD : |  |
| TOTAL FUEL : | 4,300 | FUEL USAGE : | 2,350 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Drilling 216mm hole with Bit # 3 at 1326m |
| Next 24 Hrs Op | Continue drilling to casing depth |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 3 |  |  | Drilling | 22.0 |  | Density | 1.202 | S.G. |
| Size (mm) | 216 |  |  | Tripping | 1.50 |  | Viscosity | 54 | Sec |
| Make | Reed |  |  | Surveys |  |  | Water Loss | 7.0 | Cc |
| Type | RO1APDH |  |  | Rigged up |  |  | pH | 8.5 | Strip |
| IADC Code | 4-1-7 |  |  | Testing/tools |  |  | Filter Cake | 2 | 32 nd |
| Serial Number | NDO593 |  |  | Circulate Sample |  |  | PV / YP | 20 / 34 | Cp/lb/100’ |
| Nozzles (32) | 14-14-14 |  |  | Casing |  |  | Gels | 7 / 10 | S/m |
| Depth in (m) | 1184 |  |  | Cementing |  |  | Sand | 0.30 | % Vol |
| Depth out (m) |  |  |  | Surveys |  |  | Solids | 10 | % Vol |
| Total Metres | 120 |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours | 22 |  |  | Rig Service/slip & cut | 0.50 |  | K+ | 11,550 | Mg/l |
| WOB (kg) | 9,000 |  |  | Rig down bop |  |  | Chlorides | 18,000 | Mg/l |
| RPM | 100 |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition |  |  |  | Breakdown kelly |  |  | KCL | 2.2 | % |
| Impact Force | 415 |  |  | Wait On Cement |  |  | Daily Cost $ | 2,8112 |
| Jet Velocity | 234 |  |  | Test BOPs |  |  | Cum Cost $ | 27,790 |
| B.H.A.: | BHA # 3 216mm Bit –Bit Sub-NMDC-1 x 6¼" DC-8½"Stab-7 x 6¼" Drill Collars-Drilling Jar-3 x 6¼"Drill Collars-4 x HWDP-Crossover sub |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  |  | ° at |  | m |  | Type | Amount |
| 0000 | 01.30 | Continued trip in hole washed down from 1180-1184m |  |  | ° at |  | m |  | AMC Biocde G | 1 |
| 01.30 | 10.00 | Drilled 216mm hole from 1184m to 1233m |  |  | ° at |  | m |  |  |  |
| 10.00 | 10.30 | Serviced the rig |  |  | ° at |  | m |  | Pac - R | 5 |
| 10.30 | 24.00 | Drilled 216mm hole from 1233m to1304m |  |  | ° at |  | m |  | Barite | 247 |
|  |  |  |  |  | ° at |  | m |  |  |  |
|  |  |  |  |  | ° at |  | m |  | PHPA/ KCL | 43 |
|  |  |  |  |  | ° at |  | m |  | Caustic Soda | 1 |
|  |  |  |  | PUMP 1 Duplex |  | PUMP 2 Triplex |
|  |  |  |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure | 7,200 | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP | 40 | m/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC | 70 | m/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM | 52 |  | SPM |  |
|  |  | 2 loads water |  | LPM | 325 |  | LPM |  |
|  |  | 2 hrs 8 ton tray hire Dyers |  |  |  |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 9⅝" | inch |
|  |  |  |  | Class Bulk |  |  | Weight | 36 | ppf |
|  |  |  |  | % |  |  |  | Grade | K-55 |  |
|  |  |  |  | % |  |  |  | Connection | BTC |  |
|  |  | Held BOP Drill |  | % |  |  |  | Joints | 25 |  |
|  |  |  |  | % |  |  |  | Length |  | m |
| Days since | LTA |  |  | Av. Wt |  |  | Shoe | 299m from RKB | m |

,66