LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 11 | DFS: | 11 | DATE : | 27-10-9 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1366 | LAST DEPTH : | 1304 | 24 HR PROGRESS: | 62 | PTD : |  |
| TOTAL FUEL : | 2,000 | FUEL USAGE : | 2,300 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Schlumberger running logs |
| Next 24 Hrs Op | Log-trip in hole –drill into Strezlecki sand-trip out for 7" Casing |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 3 |  |  | Drilling | 18.00 |  | Density | 1.267 | S.G. |
| Size (mm) | 216 |  |  | Tripping | 2.50 |  | Viscosity | 50 | Sec |
| Make | Reed |  |  | Surveys | 1.00 |  | Water Loss | 7.0 | Cc |
| Type | RO1APDH |  |  | Rigged up |  |  | pH | 8.5 | Strip |
| IADC Code | 4-1-7 |  |  | Testing/tools |  |  | Filter Cake | 2 | 32 nd |
| Serial Number | NDO593 |  |  | Circulate Sample |  |  | PV / YP | 18 / 35 | Cp/lb/100’ |
| Nozzles (32) | 14-14-14 |  |  | Casing |  |  | Gels | 7 / 10 | S/m |
| Depth in (m) | 1184 |  |  | Cementing |  |  | Sand | 0.70 | % Vol |
| Depth out (m) | 1366 |  |  | Surveys |  |  | Solids | 11.4 | % Vol |
| Total Metres | 182 |  |  | Circulate & Condition | 2.00 |  | Oil |  | % Vol |
| Hours | 40 |  |  | Rig Service/slip & cut | 0.50 |  | K+ | 11,550 | Mg/l |
| WOB (kg) | 9,000 |  |  | Rig down bop |  |  | Chlorides | 18,000 | Mg/l |
| RPM | 100 |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition | S.I.H |  |  | Breakdown kelly |  |  | KCL | 2.2 | % |
| Impact Force | 415 |  |  | Wait On Cement |  |  | Daily Cost $ | 207 |
| Jet Velocity | 234 |  |  | Test BOPs |  |  | Cum Cost $ | 27,997 |
| B.H.A.: | BHA # 3 216mm Bit –Bit Sub-NMDC-1 x 6¼" DC-8½"Stab-7 x 6¼" Drill Collars-Drilling Jar-3 x 6¼"Drill Collars-4 x HWDP-Crossover sub |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 1½º N60E | ° at | 1354 | m |  | Type | Amount |
| 0000 | 10.00 | Drilled 216mm hole from 1304m to 1338m |  |  | ° at |  | m |  |  |  |
| 10.00 | 10.30 | Serviced the rig |  |  | ° at |  | m |  |  |  |
| 10.30 | 18.30 | Drilled 216 mm hole from 1338m to 1366m |  |  | ° at |  | m |  | Pac - R | 1 |
| 18.30 | 19.30 | Circulated bottoms up |  |  | ° at |  | m |  | Barite | 23 |
| 19.30 | 21.00 | Wiper tripped hole to 1127m –tripped back in no fill |  |  | ° at |  | m |  |  |  |
| 21.00 | 22.00 | Circulated |  |  | ° at |  | m |  |  |  |
| 22.00 | 23.00 | Ran survey at 1354m |  |  | ° at |  | m |  |  |  |
| 23.00 | 24.00 | Tripped out for logging to 1127m |  |  |  |  |
|  |  |  |  | PUMP 1 Duplex |  | PUMP 2 Triplex |
|  |  |  |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure | 7,200 | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP | 40 | m/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC | 70 | m/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM | 52 |  | SPM |  |
|  |  |  |  | LPM | 325 |  | LPM |  |
|  |  | Two trucks of drilling mud arrived |  |  |  |  |
|  |  | Truckload 4½" Casing arrived |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 9⅝" | inch |
|  |  |  |  | Class Bulk |  |  | Weight | 36 | ppf |
|  |  |  |  | % |  |  |  | Grade | K-55 |  |
|  |  |  |  | % |  |  |  | Connection | BTC |  |
|  |  | Held BOP Drill |  | % |  |  |  | Joints | 25 |  |
|  |  |  |  | % |  |  |  | Length |  | m |
| Days since | LTA |  |  | Av. Wt |  |  | Shoe | 299m from RKB | m |

,66