LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 27 | DFS: | 27 | DATE : | 12-11-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 2,500 | LAST DEPTH : | 2,500 | 24 HR PROGRESS: |  | PTD : | Total Depth |
| TOTAL FUEL : | 4,500 | FUEL USAGE : | 1,050 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Rig up Schlumberger |
| Next 24 Hrs Op | Continue logging program preceding the wiper trip |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 5 Re-Run#4 | 6 New |  | Drilling |  |  | Density | 1.212 | S.G. |
| Size (mm) | 156 | 156 |  | Tripping | 6.00 |  | Viscosity | 35 | Sec |
| Make | Smith | Reed |  | Downtime ( Float ) | 5.00 |  | Water Loss |  | Cc |
| Type | MDi613 | R22AP |  | Wireline logging | 10.00 |  | pH | 8.0 | Strip |
| IADC Code |  | 5-1-7 |  | Testing/tools |  |  | Filter Cake | 4 | 32 nd |
| Serial Number | JD1042 | KD1019 |  | Circulate Sample |  |  | PV / YP | 6/6 | Cp/lb/100’ |
| Nozzles (32) | 3 x 12 | 3 x 14 |  | Casing |  |  | Gels | 4 / 7 | S/m |
| Depth in (m) | 1378 / 1478 | 2403 |  | Cementing |  |  | Sand | 0.25 | % Vol |
| Depth out (m) | / 2403 | 2500 |  | Surveys |  |  | Solids | 9.7 | % Vol |
| Total Metres | 1025 | 97 |  | Circulate & Condition | 3.00 |  | Oil |  | % Vol |
| Hours | 123 | 38.5 |  | Rig Service/slip & cut |  |  | K+ | 31,500 | Mg/l |
| WOB (kg) | 2,000/5000 | 10-18k |  | Rig up/ d own bop |  |  | Chlorides | 36,000 | Mg/l |
| RPM | 90 /100 | 90 |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition | 1-2-ER-A-X-2mm-NO-HRS | 3-3-ER-A-E-1-TD |  | Reaming |  |  | KCL | 6.0 | % |
| Impact Force | 237 | 176 |  | Wait On Cement |  |  | Daily Cost $ | 6,599 |
| Jet Velocity | 215 | 158 |  | Test BOPs |  |  | Cum Cost $ | 73,953 |
| B.H.A.: 5 | 156mm Bit-NBS-NMDC-1 x DC-STB-13 x DC-Jars-2 xDC |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 1½º N60E | ° at | 1354 | m |  | Type | Amount |
| 0000 | 00.30 | Schlumberger rigged down run # 1 tools |  | 4ºN340W | ° at | 1768 | m |  | AMC Pac L |  |
| 00.30 | 09.30 | Schlumberger ran log # 2 FMI-PPC –Sonic scanner |  | 12ºN340W | ° at | 2093 | m |  | AMC Pac R |  |
|  |  | Logging difficulties occurred at 2196 and 2111m |  | 18.5 | ° at | 2235 | m |  | Lakes Pac R |  |
| 09.30 | 10.00 | Rigged down Schlumberger |  | N340W | ° at |  | m |  | Xan Bore |  |
| 10.00 | 12.00 | Made up 156mm bit tripped in hole to 360m |  |  | ° at |  | m |  | Bayrtes | 28 |
| 12.00 | 13.30 | Tripped back out Float in stalled upside down |  |  | ° at |  | m |  | Potassium Chloride | 181 |
| 13.30 | 15.00 | Tripped back in hole to 360m |  |  | ° at |  | m |  | AMC Biocide G |  |
|  |  | Note 10.00hrs to 15.00hrs Contractor downtime |  |  |  |  |
| 15.00 | 18.00 | Continued trip in hole to 1365m |  | PUMP 1 Duplex |  | PUMP 2 Triplex |
| 18.00 | 18.30 | Filled pipe circulated |  | Liner | 140 | mm |  | Liner | 140 | mm |
| 18.30 | 21.00 | Tripped in hole from 1365m to 2486m |  | Pressure |  | kPa |  | Pressure | 4,300 | KPa |
| 21.00 | 21.30 | Picked up Kelly washed to bottom at 2,500m |  | A.V. DP |  | f/min |  | A.V. DP | 215 | Ft/min |
| 21.30 | 23.30 | Circulated and conditioned mud |  | A.V. DC |  | f/min |  | A.V. DC | 364 | Ft//mn |
| 23.30 | 24.00 | Slugged pipe –racked back the Kelly |  | SPM |  |  | SPM | 100 |
|  |  |  |  | GPM |  |  | GPM | 225 |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 7" | inch |
|  |  | Hunt 16 camp 4 |  | Class Bulk |  |  | Weight | 26 | ppf |
|  |  | Lakes 4 |  | % |  |  |  | Grade | K-55 |  |
|  |  | Mud logger 2 |  | % |  |  |  | Connection | BTC |  |
|  |  | Farley Riggs 4 |  | % |  |  |  | Joints | 117 |  |
|  |  | RMN 2 |  | % |  |  |  | Length | RT-Brd Hd 5.0 | m |
| Days since | LTA | Schlumberger 6 |  | Av. Wt |  |  | Shoe | 1376m from RKB | m |

,66