LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 31 | DFS: | 31 | DATE : | 16-11-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 2,500 | LAST DEPTH : | 2,500 | 24 HR PROGRESS: |  | PTD : | Total Depth |
| TOTAL FUEL : | 6,500 | FUEL USAGE : | 700 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Tripped in hole with DST tools for test at 1828m-1837m interval- rigged up surface equipment |
| Next 24 Hrs Op | Conduct DST # 4 on this well present DST run # 3 at this interval |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES @ 22.30 |
| --- | --- | --- | --- | --- |
| Bit Number |  |  |  | Drilling |  |  | Density | 1.309 | S.G. |
| Size (mm) |  |  |  | Tripping |  |  | Viscosity | 46 | Sec |
| Make |  |  |  | Downtime ( Float ) |  |  | Water Loss | 15.0 | Cc |
| Type |  |  |  | Wireline logging |  |  | pH | 8.0 | Strip |
| IADC Code |  |  |  | Testing/tools |  |  | Filter Cake | 3 | 32 nd |
| Serial Number |  |  |  | Circulate Sample |  |  | PV / YP | 15/15 | Cp/lb/100’ |
| Nozzles (32) |  |  |  | Casing |  |  | Gels | 5 / 15 | S/m |
| Depth in (m) |  |  |  | Cementing |  |  | Sand | 0.50 | % Vol |
| Depth out (m) |  |  |  | Drill stem testing | 24.00 |  | Solids | 14.6 | % Vol |
| Total Metres |  |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours |  |  |  | Rig Service/slip & cut |  |  | K+ | 36,750 | Mg/l |
| WOB (kg) |  |  |  | Rig up/ d own bop |  |  | Chlorides | 45,000 | Mg/l |
| RPM |  |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition |  |  |  | Reaming |  |  | KCL | 7.0 | % |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ | 1,971 |
| Jet Velocity |  |  |  | Test BOPs |  |  | Cum Cost $ | 84,253 |
| B.H.A.: 5 | DST Tools |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 1½º N60E | ° at | 1354 | m |  | Type | Amount |
| 0000 | 01.30 | Serviced DST tools at surface |  | 4ºN340W | ° at | 1768 | m |  | AMC Pac L |  |
| 01.30 | 07.30 | Tripped in hole with DST and 300m water cushion |  | 12ºN340W | ° at | 2093 | m |  | AMC Pac R |  |
| 07.30 | 08.30 | Rigged up surface equipment tested manifold |  | 18.5 | ° at | 2235 | m |  | Lakes Pac R |  |
| 08.30 | 09.00 | Held safety meeting |  | N340W | ° at |  | m |  | Xan Bore | 2 |
| 09.00 | 10.30 | Attempts to set Packer failed |  |  | ° at |  | m |  | Bayrtes | 135 |
| 10.30 | 11.00 | Rigged down DST surface equipment |  |  | ° at |  | m |  | Potassium Chloride |  |
| 11.00 | 17.00 | Tripped out |  |  | ° at |  | m |  | AMC Biocide G |  |
| 17.00 | 18.00 | Dismantled tools at surface |  |  |  |  |
| 18.00 | 22.30 | Wait on DST part being machined in Deer Park shop |  | PUMP 1 Duplex |  | PUMP 2 Triplex |
| 22.30 | 23.30 | Made up DST tools |  | Liner | 140 | mm |  | Liner | 140 | mm |
| 23.30 | 24.00 | Commenced trip in hole # 3 run with DST string |  | Pressure |  | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP |  | f/min |  | A.V. DP |  | Ft/min |
|  |  |  |  | A.V. DC |  | f/min |  | A.V. DC |  | Ft//mn |
|  |  |  |  | SPM |  |  | SPM |  |
|  |  |  |  | GPM |  |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 7" | inch |
|  |  | Hunt 17 camp 4 |  | Class Bulk |  |  | Weight | 26 | ppf |
|  |  | Lakes 4 |  | % |  |  |  | Grade | K-55 |  |
|  |  | Mud logger 2 |  | % |  |  |  | Connection | BTC |  |
|  |  | Farley Riggs 4 |  | % |  |  |  | Joints | 117 |  |
|  |  | RMN 1 |  | % |  |  |  | Length | RT-Brd Hd 5.0 | m |
| Days since | LTA | Schlumberger 6 |  | Av. Wt |  |  | Shoe | 1376m from RKB | m |

,66