LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 34 | DFS: | 34 | DATE : | 19-11-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 2,500 | LAST DEPTH : | 2,500 | 24 HR PROGRESS: |  | PTD : | Total Depth |
| TOTAL FUEL : | 3,400 | FUEL USAGE : | 700 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | DST # 3 A Tool open at 05.45hrs 1381m-1406m malfunction occurred ,annulus volume dropped ,indicating circ port has opened |
| Next 24 Hrs Op | Pull DST tools from DST # 3 due to test failure |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES @ 22.30 |
| --- | --- | --- | --- | --- |
| Bit Number |  |  |  | Drilling |  |  | Density | 1.248 | S.G. |
| Size (mm) |  |  |  | Tripping |  |  | Viscosity | 37 | Sec |
| Make |  |  |  | Downtime ( Float ) |  |  | Water Loss | 19.0 | Cc |
| Type |  |  |  | Wireline logging |  |  | pH | 8.0 | Strip |
| IADC Code |  |  |  | Testing/tools |  |  | Filter Cake | 3 | 32 nd |
| Serial Number |  |  |  | Circulate Sample |  |  | PV / YP | 9 / 10 | Cp/lb/100’ |
| Nozzles (32) |  |  |  | Casing |  |  | Gels | 2 / 5 | S/m |
| Depth in (m) |  |  |  | Cementing |  |  | Sand | 0.50 | % Vol |
| Depth out (m) |  |  |  | Drill stem testing | 24.00 |  | Solids | 12.4 | % Vol |
| Total Metres |  |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours |  |  |  | Rig Service/slip & cut |  |  | K+ | 23,265 | Mg/l |
| WOB (kg) |  |  |  | Rig up/ d own bop |  |  | Chlorides | 28,000 | Mg/l |
| RPM |  |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition |  |  |  | Reaming |  |  | KCL | 4.5 | % |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ | 283 |
| Jet Velocity |  |  |  | Test BOPs |  |  | Cum Cost $ | 84,725 |
| B.H.A.: 5 | 00.00-04.30 Tripped in hole for DST # 3 A 1381m- 1406m |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 1½º N60E | ° at | 1354 | m |  | Type | Amount |
| 0000 | 02.00 | Continued trip in hole for DST # 2 E 1828m-1837 |  | 4ºN340W | ° at | 1768 | m |  | AMC Pac L |  |
| 02.00 | 03.00 | Made up and tested surface equipment |  | 12ºN340W | ° at | 2093 | m |  | AMC Pac R |  |
| 03.00 | 03.30 | Set packers |  | 18.5 | ° at | 2235 | m |  | Lakes Pac R |  |
| 03.30 | 07.30 | Opened tool flowed well |  | N340W | ° at |  | m |  | Xan Bore |  |
| 07.30 | 12.30 | Shut in period |  |  | ° at |  | m |  | Bayrtes | 30 |
| 12.30 | 13.00 | Unseat packers |  |  | ° at |  | m |  | Potassium Chloride |  |
| 13.00 | 13.30 | Released drop bar-reverse circulated |  |  | ° at |  | m |  | AMC Biocide G |  |
| 13.30 | 14.30 | Circulated pumped pill rigged down surface tools |  |  |  |  |
| 14.30 | 19.00 | Tripped out with tools |  | PUMP 1 Duplex |  | PUMP 2 Triplex |
| 19.00 | 24.00 | Serviced tools changed out packer elements |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure |  | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP |  | f/min |  | A.V. DP |  | Ft/min |
|  |  |  |  | A.V. DC |  | f/min |  | A.V. DC |  | Ft//mn |
|  |  |  |  | SPM |  |  | SPM |  |
|  |  |  |  | GPM |  |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 7" | inch |
|  |  | Hunt 19 camp 4 Schlumberger on stby |  | Class Bulk |  |  | Weight | 26 | ppf |
|  |  | Lakes 4 |  | % |  |  |  | Grade | K-55 |  |
|  |  | Mud logger 2 |  | % |  |  |  | Connection | BTC |  |
|  |  | Farley Riggs 2 |  | % |  |  |  | Joints | 117 |  |
|  |  | RMN 1 |  | % |  |  |  | Length | RT-Brd Hd 5.0 | m |
| Days since | LTA | 462 |  | Av. Wt |  |  | Shoe | 1376m from RKB | m |

,66