LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 36 | DFS: | 36 | DATE : | 21-11-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 2,500 | LAST DEPTH : | 2,500 | 24 HR PROGRESS: |  | PTD : | Total Depth |
| TOTAL FUEL : | 8,300 | FUEL USAGE : | 1,100 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Cleaning out plugged DST tools ( Sand ) after trip out from test interval 1170m-1175m inside the 7 " Casing |
| Next 24 Hrs Op | Re- Run the previous test with larger water cushion |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES @ 22.30 |
| --- | --- | --- | --- | --- |
| Bit Number |  |  |  | Drilling |  |  | Density | 1.212 | S.G. |
| Size (mm) |  |  |  | Tripping |  |  | Viscosity | 40 | Sec |
| Make |  |  |  | Downtime ( Float ) |  |  | Water Loss | 22.0 | Cc |
| Type |  |  |  | Wireline logging | 4.5 |  | pH | 8.0 | Strip |
| IADC Code |  |  |  | Testing/tools |  |  | Filter Cake | 3 | 32 nd |
| Serial Number |  |  |  | Circulate Sample |  |  | PV / YP | 7 / 15 | Cp/lb/100’ |
| Nozzles (32) |  |  |  | Casing |  |  | Gels | 4 / 6 | S/m |
| Depth in (m) |  |  |  | Cementing |  |  | Sand | 0.25 | % Vol |
| Depth out (m) |  |  |  | Drill stem testing | 19.5 |  | Solids | 11.4 | % Vol |
| Total Metres |  |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours |  |  |  | Rig Service/slip & cut |  |  | K+ | 7,875 | Mg/l |
| WOB (kg) |  |  |  | Rig up/ d own bop |  |  | Chlorides | 12,000 | Mg/l |
| RPM |  |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition |  |  |  | Reaming |  |  | KCL | 1.5 | % |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ | 3,973 |
| Jet Velocity |  |  |  | Test BOPs |  |  | Cum Cost $ | 91,474 |
| B.H.A.: 5 |  |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  |  | ° at |  | m |  | Type | Amount |
| 0000 | 03.00 | Shut in tool for final build up 1451m-1477m |  |  | ° at |  | m |  | AMC Pac L |  |
| 03.00 | 04.00 | Unseated tool - reversed circulated – pumped pill |  |  | ° at |  | m |  | AMC Pac R |  |
| 04.00 | 07.30 | Tripped out with tools |  |  | ° at |  | m |  | Lakes Pac R |  |
| 07.30 | 10.00 | Serviced tools recovered gauges |  |  | ° at |  | m |  | Xan Bore | 2 |
| 10.00 | 10.30 | Rigged up Schlumberger-held meeting |  |  | ° at |  | m |  | Bayrtes | 220 |
| 10.30 | 12.00 | Ran CCL log |  |  | ° at |  | m |  | Potassium Chloride |  |
| 12.00 | 14.00 | Perforated inside 7" Casing interval 1171-1174m |  |  | ° at |  | m |  | AMC Biocide G |  |
| 14.00 | 14.30 | Rigged down Schlumberger |  |  |  |  |
| 14.30 | 15.30 | Picked up DST tools |  | PUMP 1 Duplex |  | PUMP 2 Triplex |
| 15.30 | 19.30 | Tripped in hole |  | Liner | 140 | mm |  | Liner | 140 | mm |
| 19.30 | 20.30 | Made up surface equipment –tested same |  | Pressure |  | kPa |  | Pressure |  | KPa |
| 20.30 | 21.30 | Set Packers –opened tool for 10 min-shut in pre flow |  | A.V. DP |  | f/min |  | A.V. DP |  | Ft/min |
| 21.30 | 22.00 | Unseated packer ran one stand pipe 1170-1175m |  | A.V. DC |  | f/min |  | A.V. DC |  | Ft//mn |
| 22.00 | 22.30 | Set packer opened tool for 10 min pre flow ( Bubbles ) |  | SPM |  |  | SPM |  |
| 22.30 | 23.00 | Shut in tool |  | GPM |  |  | GPM |  |
| 23.00 | 24.00 | Opened tool for main flow test ( No flow to surface ) |  |  |  |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 7" | inch |
|  |  | Hunt 18 camp 4 Schlumberger 3 |  | Class Bulk |  |  | Weight | 26 | ppf |
|  |  | Lakes 2 |  | % |  |  |  | Grade | K-55 |  |
|  |  | Mud logger 2 |  | % |  |  |  | Connection | BTC |  |
|  |  | Farley Riggs 2 |  | % |  |  |  | Joints | 117 |  |
|  |  | RMN 1 |  | % |  |  |  | Length | RT-Brd Hd 5.0 | m |
| Days since | LTA | 464 |  | Av. Wt |  |  | Shoe | 1376m from RKB | m |

,66