LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 5 | DFS: | 5 | DATE : | 21-10-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 557 m | LAST DEPTH : | 302m | 24 HR PROGRESS: | 255m | PTD : |  |
| TOTAL FUEL : |  | FUEL USAGE : |  | DAYCOST : $ |  | CUM. COST : $ | 13,951 |
| 0600 OPS : | Drilling 216mm hole at 608m |
| Next 24 Hrs Op | Drill ahead to top of Latrobe formation-run wiper trip then drill ahead to 1300m |
| Site Personnel: | Hunt Energy 19 Camp 4 Lakes Oil 5 RMN 1 Baker Mud Loggers 2 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 1 Re-run | 2 |  | Drilling | 15.0 |  | Density | 1.014 | S.G. |
| Size (mm) | 311 | 216 |  | Tripping | 5.5 |  | Viscosity | 75 | Sec |
| Make | Reed | Reed |  | Slip Cut |  |  | Water Loss |  | Cc |
| Type | EPH41 HKPR | RO1APDH |  | BHA |  |  | pH | 8.0 | Strip |
| IADC Code | 4-1-7 | 4-1-7 |  | F.I.T |  |  | Filter Cake |  | 32 nd |
| Serial Number | NR 2008 | NDO593 |  | Circulate Sample |  |  | PV / YP | 15 / 56 | Cp/lb/100’ |
| Nozzles (32) | 18-18-18 | 14-14-14 |  | Casing |  |  | Gels | 10 / 13 | S/m |
| Depth in (m) | 16 | 302 |  | Cementing |  |  | Sand |  | % Vol |
| Depth out (m) | 302 |  |  | Surveys | 1.5 |  | Solids |  | % Vol |
| Total Metres | 285 / 846 | 255 |  | Circulate & Condition | 0.5 |  | Oil |  | % Vol |
| Hours | 18.5 / 63.5 | 15 |  | Rig Service |  |  | K+ |  | Mg/l |
| WOB (kg) | 2000 | 4000 |  | Rig up/down bop |  |  | Chlorides | 1,100 | Mg/l |
| RPM | 100 | 100 |  | Drill out Cmt | 1.50 |  | PHPA |  |  |
| Condition | 2-2-NO-A-E-1-1-CT | S.I.H |  | Breakdown kelly |  |  | KCL | % |  |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ | 3,193 |
| Jet Velocity |  |  |  | Test BOPs |  |  | Cum Cost $ | 13,951 |
| B.H.A.: # 2 | 216mmBit-NBS-NMDC-Stab- 2 x 6¼" DC-Stab-6 x 6¼" DC-Supra Drilling Jar- 3 x 6¼" DC-4 x HWDP- X/O Sub Length 162.44m |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | ¾º | ° at | 32 | m |  | Type | Amount |
| 00.00 | 05.30 | Made up 216mm Drilling BHA tripped in hole to 296m |  | ½º | ° at | 96 | m |  | AMC Pac R | 2 |
| 05.30 | 07.00 | Drilled plugs –shoe at 299m-cleaned hole to 302m |  | 1º | ° at | 239 | m |  | AMC Biocide | 2 |
| 07.00 | 07.30 | Drilled 216mm hole from 302m to 305m |  | 1½º | ° at | 295 | m |  | KCL | 56 |
| 07.30 | 08.00 | Circulated hole clean with 8.4ppg mud |  | 2 | ° at | 458º | m |  | Xan Bore | 2 |
| 08.00 | 08.30 | F.I.T test with 8.4ppg mud to 12.8ppg eq |  |  | ° at |  | m |  |  |  |
| 08.30 | 12.30 | Drilled 216mm hole from 305m to 384m |  |  | ° at |  | m |  |  |  |
| 12.30 | 13.00 | Survey at 372m misrun |  |  | ° at |  | m |  |  |  |
| 13.00 | 17.30 | Drilled 216mm hole from 384m to 451m |  |  |  |  |
| 17.30 | 18.00 | Survey at 439m misrun |  | PUMP 1 |  | PUMP 2 |
| 18.00 | 18.30 | Drilled 216mm hole from 451m to 470m |  | Liner | 140 | mm |  | Liner | 140 | mm |
| 18.30 | 19.00 | Survey at 458m North 25 º East |  | Pressure |  | kPa |  | Pressure | 5,000 | KPa |
| 19.00 | 24.00 | Drilled 216mm hole from 470m to 557m |  | A.V. DP |  | m/min |  | A.V. DP | 40 | m/min |
|  |  |  |  | A.V. DC |  | m/min |  | A.V. DC | 70 | m/min |
|  |  |  |  | SPM |  |  | SPM | 140 |
|  |  |  |  | LPM |  |  | LPM / GPM | 1230 / 325 |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton | 377 |  | Size | 9⅝" | inch |
|  |  |  |  | Class Bulk |  |  | Weight | 36 | ppf |
|  |  |  |  | % |  |  |  | Grade | K-55 |  |
|  |  |  |  | % |  |  |  | Thread | BTC |  |
|  |  |  |  | % |  |  |  | Joints | 25 |  |
|  |  |  |  | % |  |  |  | Length |  | m |
| Days since | LTA |  |  | Av. Wt | 15.6 |  | Shoe | 299.00 | m |

,66