LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 1 | DFS: | 1 | DATE : | 17-10-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 23m | LAST DEPTH : | 16m | 24 HR PROGRESS: | 7m | PTD : |  |
| TOTAL FUEL : |  | FUEL USAGE : |  | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Drilling 311mm hole at 88m |
| Next 24 Hrs Op | Drill to Casing depth approx 300m |
| Site Personnel: | Hunt Energy 14 Camp 4 Lakes Oil 2 RMN 1 Baker Mud Loggers 3 Halliburton 2 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 1 Re-run |  |  | Drilling | 2.00 |  | Density | 1.032 | S.G. |
| Size (mm) | 311 |  |  | Tripping |  |  | Viscosity | 42 | Sec |
| Make | Reed |  |  | Surveys |  |  | Water Loss |  | Cc |
| Type | EPH41 HKPR |  |  | Rigged up | 22.00 |  | pH |  | Strip |
| IADC Code | 4-1-7 |  |  | Testing/tools |  |  | Filter Cake |  | 32 nd |
| Serial Number | NR 2008 |  |  | Circulate Sample |  |  | PV / YP |  | Cp/lb/100’ |
| Nozzles (32) | 18-18-18 |  |  | Casing |  |  | Gels |  | S/m |
| Depth in (m) | 16 |  |  | Cementing |  |  | Sand |  | % Vol |
| Depth out (m) |  |  |  | Surveys |  |  | Solids |  | % Vol |
| Total Metres | 7 |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours | 2 |  |  | Rig Service/slip & cut |  |  | K+ |  | Mg/l |
| WOB (kg) | 1000 |  |  | Rig down bop |  |  | Chlorides |  | Mg/l |
| RPM | 80 |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition | IN |  |  | Breakdown kelly |  |  | KCL | % |  |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ | 2,694 |
| Jet Velocity |  |  |  | Test BOPs |  |  | Cum Cost $ | 2,694 |
| B.H.A.: | 311mm Bit –NBS-8 inch drill collar |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  |  | ° at |  | m |  | Type | Amount |
| 00.00 | 05.00 | Rigging up |  |  | ° at |  | m |  | Gel | 158 |
| 05.00 | 12.30 | Drilled and installed Kelly sock |  |  | ° at |  | m |  | Caustic | 4 |
| 12.30 | 15.30 | Drilled and installed Mousehole sock |  |  | ° at |  | m |  | Soda ash | 4 |
| 15.30 | 21.00 | Continued to rig up ,ran equipment ,function tested |  |  | ° at |  | m |  |  |  |
|  |  | emergency shutdown systems, Conducted rig audit |  |  | ° at |  | m |  |  |  |
| 21.00 | 22.00 | Held pre-spud meeting |  |  | ° at |  | m |  |  |  |
| 22.00 | 24.00 | Drilled 311mm hole from 16m to 23m |  |  | ° at |  | m |  |  |  |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  | RIG ON PAYROLL AT 22.00HRS |  | Liner |  | mm |  | Liner |  | mm |
|  |  |  |  | Pressure |  | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP |  | m/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC |  | m/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM |  |  | SPM |  |
|  |  |  |  | LPM |  |  | LPM |  |
|  |  | Halliburton rigged up cementing unit |  |  |  |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 340 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 79.45 | Kg/m |
|  |  |  |  | % |  |  |  | Grade | K-55 |  |
|  |  |  |  | % |  |  |  | Connection | BTC |  |
|  |  |  |  | % |  |  |  | Joints | 1 |  |
|  |  |  |  | % |  |  |  | Length | 12.00 | m |
| Days since | LTA |  |  | Av. Wt |  |  | Shoe | 16m from RKB | m |

,66