PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 1 Date: 17-10-09

Depth: 23m Progress: 23m Days from Spud: 1

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 340mm at 15.65m

0600 hrs Update: Drill ahead with 311mm hole at 88m in Jemmy's Point Formation.

Comments: 9.375" conductor set at 12m G.L. prior to spud. Spud Wombat No.4 at 2000hrs 17th October, 2009, with 12.25" (311mm) hole.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| Spud-16 | No Samples - Conductor Section. |  |
| 16-35 | Haunted Hills Gravels - No Show | TG 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 | +23.65 +12.65 -8 | 0 0 2 Low |
| Gippsland Limestone | 137 |  |  |  |
| Lakes Entrance Formation | 625 |  |  |  |
| LaTrobe Group | 786 |  |  |  |
| Strzelecki Formation | 1311 |  |  |  |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| Spud-16 | No Samples - Conductor section |
| 16-35 | JEMMY'S POINT FORMATION SAND (90%) with minor SILTY CLAYSTONE (10%). SAND: light to medium yellow orange, very fine to very coarse, dominantly medium, subangular to rounded, poorly sorted, no cement, common to abundant grey to yellow argillaceous and silt matrix, quartzose, clear to milky quartz grains often with yellow to brown iron oxide staining, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. SILTY CLAYSTONE: medium grey, abundant dispersed very fine to coarse quartz sand grains, very soft, very dispersive, non fissile. |