PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 10 Date: 26-10-09

Depth: 1303m Progress: 119m Days from Spud: 10

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 9⅝" at 299m

0600 hrs Update: Drill ahead with 8½" hole at 1326m in LaTrobe Formation; interbedded sandstone and claystone, background gas slowly rising (at 1326m = 0.5 units).

Comments: RIH with new bit, trip gas 0.8 units, drill ahead with 8½" hole to 1303m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1184-1270 | LaTrobe Group - No Show The coal has no natural fluorescence but gives a weak dull light yellow green crush cut fluorescence. | TG 0.1-0.2u C1 99% C2 1% C3+ 0 |
| 1270-1303 | LaTrobe Group - No Show The coal has no natural fluorescence but gives a weak dull light yellow green crush cut fluorescence. | TG 0.1-0.5u C1 99% C2 1% C3+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 |  |  |  |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1184-1270 | LATROBE GROUP Sandstone (40%) interbedded with Claystone (60%) and Coal (trace). SANDSTONE: very light grey to light brown grey, very fine to grit, dominantly medium to coarse, angular to subrounded, very poorly sorted, moderate silica cement, common to abundant off white to light brown argillaceous and silt matrix, quartzose with clear to opaque quartz grains, rare green and black cherty lithics, trace black coaly detritus, trace pyrite, moderately hard, fair to good inferred porosity, no oil fluorescence. CLAYSTONE: off white to medium brown, trace medium green, often very silty and very finely arenaceous, very kaolinitic in part, slightly carbonaceous, trace black coaly flecks, trace micromica, firm to moderately hard, very dispersive, non fissile. COAL: very dark brown to dominantly black, blocky to subconchoidal fracture, earthy to slightly subvitreous lustre, slightly to moderately argillaceous, moderately hard. The coal has no natural fluorescence but gives a weak dull light yellow green crush cut fluorescence. |
| 1270-1303 | LATROBE GROUP Sandstone (20%) interbedded with Claystone (80%) and Coal (trace). SANDSTONE: very light grey to light brown grey, very fine to grit, dominantly medium to coarse, angular to subrounded, very poorly sorted, moderate silica cement, common to abundant off white to light brown argillaceous and silt matrix, quartzose with clear to opaque quartz grains, rare green and black cherty lithics, trace black coaly detritus, trace pyrite, moderately hard, fair to good inferred porosity, no oil fluorescence. CLAYSTONE: off white to medium brown, often very silty and very finely arenaceous, very kaolinitic in part, slightly carbonaceous, trace black coaly flecks, trace micromica, rare pyrite, moderately hard, very dispersive, non fissile. COAL: very dark brown to dominantly black, blocky to subconchoidal fracture, earthy to slightly subvitreous lustre, slightly to moderately argillaceous, moderately hard. The coal has no natural fluorescence but gives a weak dull light yellow green crush cut fluorescence. |