PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 11 Date: 27-10-09

Depth: 1366m Progress: 63m Days from Spud: 11

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 9⅝" at 299m

0600 hrs Update: POOH, Rig up Schlumberger for wireline logging.

Comments: Drill ahead with 8½" hole to 1366m, wiper trip, wiper trip gas 1.2 units (C1 95%, C2 4%, C3 1%, C4+ 0), POOH for wireline logging.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1303-1350 | LaTrobe Group - No Show | TG 0.1-0.2u C1 99% C2 1% C3+ 0 |
| 1350-1366 | Strzelecki Group - No Show | TG 0.1-1½u C1 96% C2 3% C3 1% C4+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 | 1350 | 1323 | 39 Low |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1303-1350 | LATROBE GROUP Sandstone (20%) interbedded with Claystone (80%). SANDSTONE: very light grey to light brown grey, very fine to grit, dominantly medium, angular to subrounded, very poorly sorted, moderate silica cement, abundant off white to light brown argillaceous and silt matrix, quartzose with clear to opaque quartz grains, rare green and black cherty lithics, trace black coaly detritus, trace pyrite, moderately hard, fair inferred porosity, no oil fluorescence. CLAYSTONE: off white to medium brown, often very silty and very finely arenaceous, very kaolinitic in part, slightly carbonaceous, trace black coaly flecks, trace micromica, tracee pyrite, moderately hard, very dispersive, slightly subfissile. |
| 1350-1366 | STRZELECKI GROUP Claystone (90%) with minor laminated Sandstone (10%). CLAYSTONE: off white to medium brown grey to medium grey to medium green grey, moderately silty, trace very fine off white altered feldspar grains, trace brown to black carbonacous specks, trace micromica, soft, very dispersive, slightly subfissile. SANDSTONE: light grey, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, weak silica cement, abundant off white argillaceous and silt matrix - matrix supported, abundant altered feldspar grains, common red brown grey and green lithics, trace quartz grains, trace very fine black carbonaceous detritus, friable, no visual porosity, no oil fluorescence. |