PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 15 Date: 31-10-09

Depth: 1450m Progress: 72m Days from Spud: 15

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 7" at 1376m

0600 hrs Update: Drill ahead with 6⅛" hole to 1478m, POOH for DST#1.

Comments: Pressure test BOP's, prepare to make up and RIH 6⅛" drilling assembly, drill 6⅛" (156mm) hole to 1381m, Perform FIT to 13.1 ppg eqmw with no leak off, drill ahead with 6⅛" hole to 1450m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1378-1478 | Strzelecki Formation - Gas Show The interval from 1378-1478m appears to be gas saturated. From visual cuttings examination most of this unit has very poor to poor visual porosity, however better quality sands are located at 1386-1388m, 1427-1433m, 1455-1457m, 1470-1473m, with visual porosity estimates for these sands assessed as fair (see cuttings description reports for more detail). The gas analysis at the top of the interval is C1 57%, C2 9%, C3 12%, C4 14%, C5 8%, with a gradual reduction in the percentages of the heavier gases to C1 93%, C2 4%, C3 2%, C4 1%, C5 0.4% at the base of this interval. An assessment based on drill and gas analysis data would suggest testing on this interval is warranted to positively ascertain flow potential. | TG 10-121u C1 57% C2 9% C3 12% C4 14% C5 8% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 | 1350 | 1323 | 39 Low |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1378-1478 | STRZELECKI FORMATION Sandstone (80%) interbedded with Claystone (20%). SANDSTONE: light grey, very fine to occasionally medium, dominantly fine, subangular to subrounded, moderately sorted, moderate silica cement, abundant off white argillaceous matrix, abundant altered feldspar grains and red brown grey and green lithics, 10% quartz grains, trace coarse brown mica flakes, trace very fine black carbonaceous detritus, trace pyrite, friable, very poor to poor visual porosity, no oil fluorescence, with the better porosity interbeds at 1386-1388m, 1427-1433m, 1455-1457m, 1470-1473m being: SANDSTONE: light grey to light green grey, very fine to medium, dominantly medium, subangular to subrounded, moderately sorted, moderate silica cement, weak calcareous cement in part, common off white argillaceous matrix, abundant altered feldspar grains and red brown grey and green lithics, 20% quartz grains, trace coarse brown mica flakes, trace very fine black carbonaceous detritus, trace pyrite, friable, fair visual porosity, no oil fluorescence. CLAYSTONE: light to medium green grey to medium grey, occasionally to medium brown grey, moderately silty, trace very fine off white altered feldspar grains, trace brown to black carbonacous specks, trace micromica, firm, very dispersive, slightly subfissile. |