PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 17 Date: 2-11-09

Depth: 1478m Progress: 0m Days from Spud: 17

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 7" at 1376m

0600 hrs Update: Finish FSI, unseat packers, reverse circulate contents of string - recovered rathole mud (no field identifiable water oil or condensate in the rathole mud), POOH with test tools.

Comments: RIH, run DST#1, Packer set in casing at 1373m to test interval 1376-1478m, tool opened with weak blow, packer kept sliding and closing tool, packers unseated and reset in open hole at 1383m, DST#1 1383-1478m, tool opened with strong blow to bottom of bucket, IF 15 mins, ISI 90 mins, FF 180 mins, FSI 540 mins, GTS 5 mins into FF at a maximum flowing pressure of 6PSI through a ¼" choke (RTSM).

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
|  | No new formation drilled. |  |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 | 1350 | 1323 | 39 Low |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
|  | No new formation drilled. |