PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 19 Date: 4-11-09

Depth: 1805m Progress: 254m Days from Spud: 19

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 7" at 1376m

0600 hrs Update: Drill ahead with 6¼" hole at 1876m. GAS SHOW: The interval from 1832-1835m appears to be gas saturated. From visual cuttings examination this interval has fair visual porosity with the sands having less white clay matrix than the over and underlying sands. Gas readings in this interval reached 379 units (C1 97%, C2 2.0%, C3 0.6%, C4 0.2%, C5 0.1%) - no oil fluorescence was observed. An assessment based on drill and gas analysis data would suggest further evaluation of this interval may be warranted to positively ascertain flow potential.

Comments: Drill ahead with 6¼" hole to 1781m, survey at 1768m = 3½° S5°E, wiper trip, wiper trip gas 46 units, drill ahead with 6¼" hole to 1805m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1551-1600 | Strzelecki Formation - Gas Show The interval from 1551-1600m appears to be gas saturated. From visual cuttings examination most of this unit has very poor to poor visual porosity sands interbedded with Claystone (70%), however within this interval better quality sands with poor to fair visual porosity are located at: 1560-1562m with TG = 122u, 1580-1581m with TG = 60u, 1584-1586m with TG = 155u. An assessment based on drill and gas analysis data would suggest further evaluation on this interval is warranted to positively ascertain flow potential. Possible gas/water contact present at approximately 1600m. | TG 20-155u C1 95% C2 3.2% C3 1.3% C4 0.5% C5 0.2% |
| 1600-1650 | Strzelecki Formation - No Show | TG 10-25u C1 95.8% C2 2.8% C3 0.9% C4 0.3% C5 0.2% |
| 1650-1805 | Strzelecki Formation - No Show | TG 10-51u C1 96.3% C2 2.5% C3 0.8% C4 0.3% C5 0.1% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 | 1350 | 1323 | 39 Low |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1551-1600 | STRZLECKI FORMATION Sandstone (30%) inerbedded with Claystone (70%) and Coal (trace). SANDSTONE: light green grey, very fine to medium, dominantly fine to medium, subangular to subrounded, moderately sorted, moderate silica cement, weak calcareous cement in part, common to abundant off white argillaceous matrix, abundant altered feldspar grains and red brown grey and green lithics, common quartz grains, trace coarse brown mica flakes, trace very fine black carbonaceous detritus, friable, nil to occasionally fair visual porosity, no oil fluorescence. CLAYSTONE: light to medium green grey to medium grey to medium brown grey, moderately to very silty grading to argillaceous siltstone in part, very finely arenaceous in part, trace very fine off white altered feldspar grains, trace to common brown to black carbonaceous specks and coaly detritus, trace micromica, firm, very dispersive, slightly subfissile. COAL: very dark brown to black, earthy to subvitreous lustre, blocky to platy fracture, moderately to very argillaceous, hard, brittle. |
| 1600-1650 | STRZLECKI FORMATION Sandstone (50%) inerbedded with Claystone (50%). SANDSTONE: light green grey, very fine to medium, dominantly medium, subangular to subrounded, moderately sorted, moderate silica cement, weak calcareous cement in part, abundant off white argillaceous matrix, abundant altered feldspar grains and red brown grey and green lithics, common quartz grains, trace coarse brown mica flakes, trace black coaly detritus, friable, poor visual porosity, no oil fluorescence. CLAYSTONE: light to medium grey to medium green grey to medium brown grey, moderately to very silty grading to argillaceous siltstone in part, very finely arenaceous in part, trace very fine off white altered feldspar grains, common brown to black carbonaceous specks and coaly detritus, trace micromica, firm, very dispersive, slightly subfissile. |
| 1650-1805 | STRZLECKI FORMATION Sandstone (40%) inerbedded with Claystone (60%). SANDSTONE: light green grey, very fine to occasionally medium, dominantly fine, subangular to subrounded, moderately sorted, moderate silica cement, moderate to strong calcareous cement in part, abundant off white argillaceous matrix, abundant altered feldspar grains and red brown grey and green lithics, trace to common quartz grains, trace coarse brown mica flakes, trace black coaly detritus, trace to common calcite infilled fractures, friable, nil to poor visual porosity, no oil fluorescence. CLAYSTONE: light to medium green grey to medium grey to medium brown grey, moderately to very silty grading to argillaceous siltstone in part, very finely arenaceous in part, trace very fine off white altered feldspar grains, trace to common brown to black carbonaceous specks and coaly detritus, trace micromica, trace to common calcite infilled fractures, firm to moderately hard, very dispersive, subfissile. |