PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 2 Date: 18-10-09

Depth: 302m Progress: 279m Days from Spud: 2

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 340mm at 15.65m

0600 hrs Update: Rig up to run 244mm (9.625") casing.

Comments: Drill ahead with 311mm (12.25") hole to 302m, wiper trip to 105m to condition hole, POOH for 244mm (9.625") casing.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 35-125 | Jemmy's Point Formtion - No Show | TG Trace C1 100% |
| 125-145 | Tambo River Formation - No Show | TG Trace C1 100% |
| 145-302 | Gippsland Limestone - No Show | TG Trace C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 |  |  |  |
| LaTrobe Group | 786 |  |  |  |
| Strzelecki Formation | 1311 |  |  |  |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 35-125 | JEMMY'S POINT FORMATION Massive Sandstone (100%). SANDSTONE: light to medium grey, very fine to very coarse, dominantly medium, subangular to rounded, dominantly rounded, poorly sorted, no cement, trace to common medium grey argillaceous and silt matrix at top - increasing to common to abundant with depth, quartzose with clear to opaque quartz grains often with grey brown staining, common grey to black to brown cherty lithics, trace to common coarse clear to brown mica flakes, trace black coaly detritus, unconsolidated, good to very good inferred porosity, no oil fluorescence. |
| 125-145 | TAMBO RIVER FORMATION Massive Marl (100%). MARL: light to medium grey to medium green grey to medium brown grey, common to abundant fossil fragments including bryozoa, shell fragments, echinoid spines, forams and sponge spicules, very soft, very dispersive, non fissile. |
| 145-302 | GIPPSLAND LIMESTONE Massive Calcarenite (100%) CALCARENITE: light grey to light brown grey, rarely light green grey, fine to medium occasionally coarse grained, weak calcareous cement, common to abundant fossil fragments including bryozoa, forams, shell fragments and echinoid spines, slightly to occasionally moderately argillaceous, trace very fine to fine quartz sand grains, trace green glauconite, friable, poor visual porosity, no oil fluorescence. |