PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 20 Date: 5-11-09

Depth: 2029m Progress: 224m Days from Spud: 20

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 7" at 1376m

0600 hrs Update: Drill ahead with 6¼" hole at 2058m. Interval 2029-2055 - Strzelecki Formation, Sandstone (95%) interbedded with minor Claystone (5%), background gas 10-25 units, no shows.

Comments: Drill ahead with 6¼" hole to 2029m. Possible major fault intersection at 1863m. What is described as "red mineral" in cuttings descriptions is most likely "geothite" which is a primary hydrothermal mineral FeO(OH).

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1805-1832 | Strzelecki Formation - No Show | TG 20-155u C1 96% C2 2.4% C3 0.8% C4 0.3% C5 0.1% |
| 1832-1835 | Strzelecki Formation - Gas Show The interval from 1832-1835m appears to be gas saturated. From visual cuttings examination this interval has fair visual porosity with the sands having slightly less white clay matrix than the over and underlying sands, however the cuttings samples also indicate the possibility for this interval to contain a possible fracture/fault as evidenced by calcite veining in the cuttings samples. An assessment based on drill and gas analysis data would suggest further evaluation of this interval may be warranted to positively ascertain flow potential. | TG 379u C1 97% C2 2.0% C3 0.6% C4 0.2% C5 0.1% |
| 1835-1863 | Strzelecki Formation - No Show | TG 20-45u C1 96% C2 2.5% C3 0.8% C4 0.3% C5 0.1% |
| 1863-1885 | Strzelecki Formation - No Show Possible major fault intersection at 1863m. | TG 18-50u C1 96% C2 2.7% C3 0.9% C4 0.3% C5 0.1% |
| 1885-1943 | Strzelecki Formation - No Show | TG 18-45u C1 94.9% C2 3.4% C3 1.2% C4 0.4% C5 0.1% |
| 1943-1945 | Strzelecki Formation - Gas Show The interval from 1943-1945 appears to be gas saturated with the gas coming from a possible fracture/fault zone, as evidenced by red mineral and calcite veining and temperature/solution alteration of the surrounding sediments. Maximum gas recorded 95 units. | TG 95u C1 96.5% C2 2.4% C3 0.8% C4 0.2% C5 0.1% |
| 1945-1971 | Strzelecki Formation - No Show | TG 18-45u C1 95.2% C2 3.1% C3 1.2% C4 0.4% C5 0.1% |
| 1971-1972 | Strzelecki Formation - Gas Show The interval from 1943-1945 appears to be gas saturated with the gas coming from a possible fracture/fault zone, as evidenced by red mineral and calcite veining and temperature/solution alteration of the surrounding sediments. Maximum gas recorded 120 units | TG 120u C1 96.1% C2 2.6% C3 0.9% C4 0.3% C5 0.1% |
| 1972-2029 | Strzelecki Formation - No Show | TG 12-30u C1 93.7% C2 3.7% C3 1.6% C4 0.7% C5 0.3% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 | 1350 | 1323 | 39 Low |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1805-1832 | STRZLECKI FORMATION Sandstone (60%) interbedded with Claystone (40%). SANDSTONE: light to medium green grey, very fine to occasionally medium, dominantly fine, subangular to subrounded, moderately sorted, moderate silica cement, moderate to strong calcareous cement in part, abundant off white to medium green argillaceous matrix, abundant altered feldspar grains and red brown grey and green lithics, trace to common quartz grains, trace coarse brown mica flakes, trace black coaly detritus, trace calcite infilled fractures, friable, poor visual porosity, no oil fluorescence. CLAYSTONE: light to medium grey to medium green grey to medium brown grey, moderately to very silty, very finely arenaceous in part, trace very fine off white altered feldspar grains, trace to common brown to black carbonaceous specks and coaly detritus, trace micromica, trace calcite infilled fractures, moderately hard, very dispersive, subfissile. |
| 1832-1835 | STRZLECKI FORMATION Sandstone (100%). SANDSTONE: light green grey to medium green, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, moderate silica cement, moderate calcareous cement in part, common to abundant off white to medium green argillaceous matrix, abundant altered feldspar grains and red brown grey and green lithics, common quartz grains, trace coarse brown mica flakes, trace black coaly detritus, trace calcite infilled fractures, friable, fair visual porosity, no oil fluorescence. |
| 1835-1863 | STRZLECKI FORMATION Sandstone (50%) interbedded with Claystone (50%). SANDSTONE: light to medium green grey, very fine to fine, dominantly fine, subangular to subrounded, moderately sorted, moderate silica cement, moderate calcareous cement in part, abundant off white to medium green argillaceous matrix, abundant altered feldspar grains and red brown grey and green lithics, trace quartz grains, trace coarse brown mica flakes, trace black coaly detritus, trace calcite infilled fractures, friable, very poor visual porosity, no oil fluorescence. CLAYSTONE: light to medium grey to medium green grey to medium brown grey, moderately to very silty, very finely arenaceous in part, trace very fine off white altered feldspar grains, trace to common brown to black carbonaceous specks and coaly detritus, trace micromica, rare calcite infilled fractures, moderately hard, very dispersive, subfissile. |
| 1863-1885 | STRZLECKI FORMATION Sandstone (80%) interbedded with Claystone (20%) and Coal (Trace) - possibly hot water solution mineral alteration to this interval. SANDSTONE: off white to light green grey to light pink, very fine to fine, dominantly fine, subangular to subrounded, moderately to well sorted, strong silica cement, weak calcareous cement in part, abundant off white to pink argillaceous matrix, abundant white and pink feldspar grains, common green red brown grey and black lithics, trace quartz grains, trace coarse green brown mica flakes, trace black coaly detritus, trace calcite infilled fractures, hard, no visual porosity, no oil fluorescence. CLAYSTONE: light to medium grey to medium green grey to medium brown grey, moderately to very silty, very finely arenaceous in part, trace very fine off white altered feldspar grains, trace to common brown to black carbonaceous specks and coaly detritus, trace micromica, rare calcite infilled fractures, moderately hard, very dispersive, subfissile. COAL: black, earthy to vitreous, platy fracture, slightly argillaceous, hard, brittle. |
| 1885-1943 | STRZELECKI FORMATION Claystone (90%) interbedded with Sandstone (10%) CLAYSTONE: light to dominantly medium grey, occasionally medium green grey to medium brown grey, moderately to very silty, very finely arenaceous in part, trace to common very fine off white altered feldspar grains in part, trace to common brown to black carbonaceous specks and coaly detritus in part, trace to common micromica, rare calcite infilled fractures, moderately hard, very dispersive, subfissile. SANDSTONE: off white to light green grey, very fine, subangular to subrounded, moderately sorted, moderate silica cement, weak calcareous cement in part, abundant off white argillaceous matrix - matrix supported, abundant altered feldspar grains, trace red brown grey and green lithics, trace quartz grains, trace black coaly detritus, trace calcite infilled fractures, friable, no visual porosity, no oil fluorescence. |
| 1943-1945 | STRZLECKI FORMATION Sandstone (30%) interbedded with Claystone (70%) - possibly hot water solution mineral alteration to this interval. CLAYSTONE: light to medium grey to occasionally medium brown grey, moderately to very silty, very finely arenaceous in part, trace to common very fine off white altered feldspar grains, trace to common brown to black carbonaceous specks and coaly detritus, common micromica, trace calcite infilled fractures, moderately hard, very dispersive, subfissile. SANDSTONE: off white to light green grey, very fine to rarely medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica cement, moderate calcareous cement in part, abundant off white to occasionally pink argillaceous matrix, abundant white and occasional pink feldspar grains, common green red brown grey and black lithics, trace quartz grains, trace coarse green brown mica flakes, trace black coaly detritus, trace calcite and red mineral veining, hard, no visual intergranular porosity, no oil fluorescence. |
| 1945-1971 | STRZELECKI FORMATION Sandstone (80%) interbedded with Claystone (20%) SANDSTONE: off white to light green grey, very fine to occasionally medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica cement, moderate calcareous cement in part, abundant off white argillaceous matrix, abundant white and common pink feldspar grains, common green red brown grey and black lithics, 10% quartz grains, rare coarse green brown mica flakes, trace black coaly detritus, trace calcite and red mineral veining, hard, no visual intergranular porosity, no oil fluorescence. CLAYSTONE: light to medium grey to occasionally medium brown grey, moderately to very silty, very finely arenaceous in part, trace to common very fine off white altered feldspar grains, trace to common brown to black carbonaceous specks and coaly detritus, common micromica, trace calcite infilled fractures, moderately hard, very dispersive, subfissile. |
| 1971-1972 | STRZLECKI FORMATION Sandstone (100%) interbedded with Claystone (Trace) - possibly hot water solution mineral alteration to this interval. SANDSTONE: off white to light green grey to pink, very fine to occasionally medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica cement, moderate calcareous cement in part, abundant off white and pink argillaceous matrix, abundant white and pink feldspar grains, common green red brown grey and black lithics, 10% quartz grains, trace black coaly detritus, common calcite and red mineral veining, hard, no visual intergranular porosity, no oil fluorescence. CLAYSTONE: light to medium grey to occasionally medium brown grey, moderately to very silty, very finely arenaceous in part, trace to common very fine off white altered feldspar grains, trace to common brown to black carbonaceous specks and coaly detritus, common micromica, trace calcite and red mineral infilled fractures, moderately hard, very dispersive, subfissile. |
| 1972-2029 | STRZLECKI FORMATION Sandstone (90%) interbedded with Claystone (10%) - possibly hot water solution mineral alteration to this interval. SANDSTONE: off white to light green grey light pinkish grey, very fine to occasionally medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica cement, strong calcareous cement in part, abundant off white and trace pink argillaceous matrix, abundant white and pink feldspar grains, common green red brown grey and black lithics, 10% quartz grains, rare black coaly detritus, common calcite and red mineral veining, hard, no visual intergranular porosity, no oil fluorescence. CLAYSTONE: light to medium grey to occasionally medium brown grey, moderately to very silty, very finely arenaceous in part, trace to common very fine off white altered feldspar grains, trace to common brown to black carbonaceous specks and coaly detritus, common micromica, trace calcite and red mineral infilled fractures, common slickensides, moderately hard, very dispersive, subfissile. |