PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 21 Date: 6-11-09

Depth: 2029m Progress: 115m Days from Spud: 21

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 7" at 1376m

0600 hrs Update: Drill ahead with 6¼" hole at 2175m. Current lithology Strzelecki sandstone (90%) interbedded with minor claystone (10%), no shows.

Comments: Drill ahead with 6¼" hole to 2105m, survey, deviation at 2090m = 12°, wiper trip, wiper trip gas = 33 units, drill ahead with 6¼" hole to 2144m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 2029-2144 | Strzelecki Formation - No Show The coal detritus in the sandstone and claystone has no natural fluorescence but gives a moderately bight slow streaming to crush milky white cut fluorescence. The minor gas peaks within this interval are associated with increased coal detritus in the cuttings samples. | TG 10-55u C1 93.7% C2 3.7% C3 1.6% C4 0.7% C5 0.3% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 | 1350 | 1323 | 39 Low |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 2029-2112 | STRZLECKI FORMATION Sandstone (90%) interbedded with Claystone (10%). SANDSTONE: off white to light green grey, light pinkish grey, very fine to occasionally medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica cement, strong calcareous cement in part, abundant off white and trace pink argillaceous matrix, abundant white and pink feldspar grains, common green red brown grey and black lithics, 10% quartz grains, trace green brown mica flakes, trace to common black coaly detritus, trace to common calcite and red mineral veining, hard, no visual intergranular porosity, no oil fluorescence. CLAYSTONE: medium green grey to medium grey to medium brown grey, moderately to very silty, very finely arenaceous in part, trace to common very fine off white altered feldspar grains, trace to common brown to black carbonaceous specks and coaly detritus, common micromica, trace calcite and red mineral infilled fractures, common slickensides, moderately hard, very dispersive, subfissile. CUT: the coal detritus in the sandstone and claystone has no natural fluorescence but gives a moderately bight slow streaming to crush milky white cut fluorescence. |
| 2112-2144 | STRZLECKI FORMATION Sandstone (80%) interbedded with Claystone (20%). SANDSTONE: off white to light green grey, light pinkish grey, very fine to occasionally medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica cement, strong calcareous cement in part, abundant off white and trace pink argillaceous matrix, abundant white and pink feldspar grains, common green red brown grey and black lithics, common quartz grains, trace green brown mica flakes, common to abundant black coaly detritus, trace calcite and red mineral veining, hard, no visual intergranular porosity, no oil fluorescence. CLAYSTONE: medium grey, occasionally medium green grey to medium brown grey, moderately to very silty, very finely arenaceous in part, trace to common very fine off white altered feldspar grains, common brown to black carbonaceous specks and coaly detritus, common micromica, trace calcite infilled fractures, common slickensides, moderately hard, very dispersive, subfissile. |