PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 23 Date: 8-11-09

Depth: 2400m Progress: 122m Days from Spud: 23

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 7" at 1376m

0600 hrs Update: Drill ahead with 6¼" hole to 2403m, POOH for BHA change.

Comments: Drill ahead with 6¼" hole to 2400m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 2278-2400 | Strzelecki Formation - No Show. The coal detritus in the sandstone and claystone has no natural fluorescence but gives a moderately bright slow streaming to crush milky white cut fluorescence. The 80 unit gas peak at 2326-2327m (C1 96.1%, C2 2.7%, C3 1.0%, C4 0.2%, C5 trace) within this interval corresponds with increased coal detritus in the cuttings samples, as does the increased gas (to 40 units) at 2342m, 2379m (37 units) and 2389m (30 units). | TG 10-80u C1 94.7% C2 3.5% C3 1.5% C4 0.3% C5 0.1% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 | 1350 | -1323 | 39 Low |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 2278-2367 | STRZLECKI FORMATION Sandstone (80%) interbedded with Claystone (20%) and minor Coal (Trace). SANDSTONE: off white to light green grey, light pinkish grey, very fine to rarely medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica cement, strong calcareous cement in part, abundant off white and trace pink argillaceous matrix, abundant white and pink feldspar grains, common green red brown grey and black lithics, common quartz grains, trace to abundant black coaly detritus, trace calcite and red mineral veining, hard, no visual intergranular porosity, no oil fluorescence. CLAYSTONE: medium grey to medium green grey,moderately to very silty, very finely arenaceous in part, trace to common very fine off white altered feldspar grains, trace to abundant brown to black carbonaceous specks and coaly detritus, common micromica, trace calcite and red mineral infilled fractures, common slickensides, hard, very dispersive, subfissile. COAL: very dark brown to black, earthy to vitreous, blocky to platy fracture, moderately argillaceous in part, hard, brittle. The coal has no natural fluorescence but gives a moderately bright slow streaming to crush milky white cut fluorescence. |
| 2367-2400 | STRZLECKI FORMATION Sandstone (70%) interbedded with Claystone (30%) and minor Coal (Trace). SANDSTONE: off white to light green grey, very fine to rarely medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica cement, moderate calcareous cement in part, abundant off white argillaceous matrix, abundant white altered feldspar grains, common green red brown grey and black lithics, trace to common quartz grains, trace black coaly detritus, trace calcite veining, hard, no visual intergranular porosity, no oil fluorescence. CLAYSTONE: medium to dark grey to medium green grey to medium brown grey, moderately to very silty - grades to siltstone, trace to abundant very fine off white altered feldspar grains, common to abundant dark brown to black carbonaceous specks and coaly detritus, common micromica, common slickensides, moderately hard, very dispersive, subfissile. COAL: very dark brown to black, earthy to vitreous, blocky to platy fracture, moderately argillaceous in part, hard, brittle. The coal has no natural fluorescence but gives a moderately bright slow streaming to crush milky white cut fluorescence. |