PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 24 Date: 9-11-09

Depth: 2413m Progress: 13m Days from Spud: 24

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 7" at 1376m

0600 hrs Update: Drill ahead with 6¼" hole at 2432m. Current Formation Strzelecki sandstone (70%) interbedded with Claystone (30%), background gas 2 units, no shows.

Comments: Drill ahead with 6¼" hole to 2403m, POOH for BHA change and new bit, RIH, trip gas 51 units, drill ahead with 6¼" hole to 2413m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 2400-2413 | Strzelecki Formation - No Show. | TG 2-20u C1 94.1% C2 3.3% C3 2.2% C4 0.2% C5 0.2% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 | 1350 | -1323 | 39 Low |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 2400-2413 | STRZLECKI FORMATION Sandstone (60%) interbedded with Claystone (40%). SANDSTONE: off white to light green grey, very fine to rarely medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica cement, moderate calcareous cement in part, abundant off white argillaceous matrix, abundant white altered feldspar grains, common green red brown grey and black lithics, trace to common quartz grains, trace black coaly detritus, trace calcite veining, hard, no visual intergranular porosity, no oil fluorescence. CLAYSTONE: medium to dark grey to medium green grey to medium brown grey, moderately to very silty - grades to siltstone, trace to abundant very fine off white altered feldspar grains, common to abundant dark brown to black carbonaceous specks and coaly detritus, common micromica, common slickensides, moderately hard, very dispersive, subfissile. |