PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 25 Date: 10-11-09

Depth: 2477m Progress: 64m Days from Spud: 25

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 7" at 1376m

0600 hrs Update: Drill ahead with 6¼" hole at 2493m. Current lithology Strzelecki Formation Claystone (70%) interbedded with Claystone (30%) and minor Coal (Trace), no shows.

Comments: Drill ahead with 6¼" hole to 2477m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 2413-2477 | Strzelecki Formation - No Show. The coal has no fluorescence but gives a moderately bright slow streaming to crush milky white cut fluorescence. | TG 2-18u C1 94.1% C2 3.3% C3 2.2% C4 0.2% C5 0.2% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 | 1350 | -1323 | 39 Low |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 2413-2477 | STRZLECKI FORMATION Sandstone (50%) interbedded with Claystone (50%), with minor Coal (trace). SANDSTONE: off white to light green grey, very fine to rarely medium, dominantly fine, subangular to subrounded, moderately sorted, very strong silica cement, moderate calcareous cement in part, abundant off white argillaceous matrix, abundant white altered feldspar grains, common green red brown grey and black lithics, trace quartz grains, trace black coaly detritus, trace calcite and red mineral veining, very hard, no visual intergranular porosity, no oil fluorescence. CLAYSTONE: medium to dark grey to medium green grey to medium brown grey, moderately to very silty - grades to siltstone, common to abundant very fine off white altered feldspar grains, common dark brown to black carbonaceous specks and coaly detritus, common micromica, common slickensides, hard, moderatel dispersive, subfissile. COAL: very dark brown to black, earthy to vitreous, blocky to dominantly platy fracture - often slickensided, slightly argillaceous in part, hard, brittle. The coal has no fluorescence but gives a moderately bright slow streaming to crush milky white cut fluorescence. |