PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 26 Date: 11-11-09

Depth: 2500m Progress: 23m Days from Spud: 26

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 7" at 1376m

0600 hrs Update: Continue Wireline Logging - Run#1 HMGS-PEX-HRLA, RIH with Run#2 Sonic-Scanner-FMI (hole sticky).

Comments: Drill ahead with 6¼" hole to 2500m. Reached T.D. 2500m at 0845 hrs, 11th November, 2009. Circulate hole clean, wiper trip to condition hole - wiper trip gas 6 units - POOH for wireline logs, Rig up Schlumberger, Run#1 HMGS-PEX-HRLA.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 2477-2500 T.D. | Strzelecki Formation - No Show. The coal has no fluorescence but gives a moderately bright slow streaming to crush milky white cut fluorescence. | TG 2-15u C1 94.4% C2 3.2% C3 2.1% C4 0.2% C5 0.1% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 | 1350 | -1323 | 39 Low |
| Total Depth | 2004 | 2500 | -2473 | 496 Low |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 2477-2500 T.D. | STRZLECKI FORMATION Claystone (60%) interbedded with Sandstone (40%), with minor Coal (trace). CLAYSTONE: medium to occasionally dark grey to medium brown grey, occasionally medium green grey, moderately to very silty - grades to siltstone in part, abundant very fine off white altered feldspar grains in part, common dark brown to black carbonaceous specks and coaly detritus, common micromica, common slickensides, hard, moderately dispersive, subfissile. SANDSTONE: off white to light green grey, very fine to rarely medium, dominantly fine, subangular to subrounded, moderately sorted, very strong silica cement, moderate calcareous cement in part, abundant off white argillaceous matrix, abundant white altered feldspar grains, common green red brown grey and black lithics, trace to common quartz grains, trace black coaly detritus, trace calcite and red mineral veining, very hard, no visual intergranular porosity, no oil fluorescence. COAL: very dark brown to black, earthy to vitreous, blocky to dominantly platy fracture - often slickensided, slightly argillaceous in part, hard, brittle. The coal has no fluorescence but gives a moderately bright slow streaming to crush milky white cut fluorescence. |