PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 5 Date: 21-10-09

Depth: 557m Progress: 255m Days from Spud: 5

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 9⅝" at 299m

0600 hrs Update: Drill ahead with 8½" hole at 608m.

Comments: RIH with 216mm (8½") drilling assembly, drill out plugs and shoe track, drill new hole to 305m, perform FIT to 12.8 EMW, drill ahead with 8½" hole to 557m. Deviation at 472m = 2° at 25°NE.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 302-605 | Gippsland Limestone - No Show | TG Trace C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 |  |  |  |
| LaTrobe Group | 786 |  |  |  |
| Strzelecki Formation | 1311 |  |  |  |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 302-575 | GIPPSLAND LIMESTONE. Massive Calcarenite (100%). CALCARENITE: off white to light medium grey to light brown grey, fine to medium grained, weak to moderate rarely strong calcareous cement, abundant bryozoa and echinoid spines, trace forams, and shell fragments, non to moderately argillaceous, rare very fine to fine quartz sand grains, common green glauconite, friable, poor visual porosity, no oil fluorescence. |
| 575-595 | GIPPSLAND LIMESTONE Calcarenite (70%) grading to Calcilutite (30%). CALCARENITE: light to medium grey to medium brown grey, very fine to fine grained, very calcilutitic in part - grades to calcilutite, weak to moderate calcareous cement, trace bryozoa, echinoid spines and forams, slightly to often very argillaceous, trace green glauconite, soft to friable, very poor visual porosity, no oil fluorescence. CALCILUTITE: light grey to medium grey to medium brown grey, slightly to very argillaceous, often very finely calcarenitic - grades to calcarenite, trace fossil fragments, soft, sticky, non fissile. |
| 595-605 | GIPPSLAND LIMESTONE Calcarenite (30%) grading to Calcilutite (50%) grading to Marl (20%) CALCARENITE: light to medium grey to medium brown grey, very fine to fine grained, very calcilutitic in part - grades to calcilutite, weak to moderate calcareous cement, trace bryozoa, echinoid spines and forams, slightly to often very argillaceous - grades to marl, trace green glauconite, soft to friable, very poor visual porosity, no oil fluorescence. CALCILUTITE: light grey to medium grey to medium brown grey, slightly to very argillaceous - grades in part to marl, often very finely calcarenitic - grades to calcarenite, trace fossil fragments, soft, sticky, non fissile. MARL: medium grey to medium brown, very calcareous grading to calcilutite, trace fossil fragments, soft, sticky, non fissile. |