PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 6 Date: 22-10-09

Depth: 557m Progress: 190m Days from Spud: 6

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 9⅝" at 299m

0600 hrs Update: Continue Wiper Trip, drill ahead with 8½" hole at 778m in Lakes Entrance Formation.

Comments: Drill ahead with 8½" hole to 747m, wiper trip. Survey at 687m = 2° at 86°E.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 605-627 | Gippsland Limestone - No Show | TG Trace C1 100% |
| 627-747 | Lakes Entrance Formation - No Show | TG 0.7u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 |  |  |  |
| Strzelecki Formation | 1311 |  |  |  |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 605-627 | GIPPSLAND LIMESTONE Calcilutite (60%) grading to Calcarenite (20%) grading to Marl (20%). CALCARENITE: light to medium grey to medium brown grey, very fine to fine grained, very calcilutitic in part - grades to calcilutite, weak to moderate calcareous cement, trace bryozoa, echinoid spines and forams, slightly to often very argillaceous - grades to marl, trace green glauconite, soft to friable, very poor visual porosity, no oil fluorescence. CALCILUTITE: light grey to medium grey to medium brown grey, slightly to very argillaceous - grades in part to marl, often very finely calcarenitic - grades to calcarenite, trace fossil fragments, soft, sticky, non fissile. MARL: medium grey to medium brown, very calcareous grading to calcilutite, trace fossil fragments, soft, sticky, non fissile. |
| 627-705 | LAKES ENTRANCE FORMATION Massive Marl (100%). MARL: light to medium grey to green grey to brown grey, very calcareous - grades in part to off white argillaceous calcilutite, trace fossil fragments, soft, sticky, non fissile. |
| 705-747 | LAKES ENTRANCE FORMATION Massive Marl (100%). MARL: very light to medium green grey to light to medium grey, occasionally light to medium brown grey, moderately to very calcareous, trace fossil fragments, soft, sticky, non fissile. |