PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 7 Date: 23-10-09

Depth: 967m Progress: 404m Days from Spud: 7

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 9⅝" at 299m

0600 hrs Update: Drill ahead with 8½" hole at 1044m, in LaTrobe Formation (no shows).

Comments: Continue Wiper Trip, drill ahead with 8½" hole to 967m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 747-820 | Lakes Entrance Formation - No Show | TG 0.7u C1 94% C2 4% C3 2% C4+ 0 |
| 820-855 | LaTrobe Group - No Show | TG 2-6u C1 97% C2 Trace C3 2% C4 1% |
| 855-967 | LaTrobe Group - No Show | TG 0.2-2u C1 97% C2 2% C3 1% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 |  |  |  |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 747-820 | LAKES ENTRANCE FORMATION Massive Marl (100%). MARL: light to medium green grey to medium grey to medium brown grey, moderately to very calcareous, trace fossil fragments, trace to common glauconite - increases with depth, soft, sticky, non fissile. |
| 820-855 | LATROBE GROUP Coal (20%) interbedded with and grading to Claystone (70%) grading to Sandstone (10%). COAL: medium brown to black, irregular to blocky fracture, earthy lustre, slightly to very argillaceous, firm to moderately hard. CLAYSTONE: light to medium brown, very slightly carbonaceous, trace black coaly flecks, trace light brown cryptocrystalline ankerite, trace pyrite, soft, very dispersive, non fissile. Note: trace dull yellow orange mineral fluorescence from ankerite. SANDSTONE: light to medium brown, very fine to medium grained, dominantly very fine, angular to subrounded, poor to moderate sorting, very weak silica cement, abundant light brown argillaceous and silt matrix, quartzose with clear to opaque quartz grains often with brown argillaceous staining, trace coarse clear mica flakes, trace black coaly detritus, rare pyrite, friable, very poor inferred porosity, no oil fluorescence. |
| 855-967 | LATROBE GROUP Sandstone (60%) interbedded with Claystone (30%) and Coal (10%). COAL: medium brown to black, irregular to blocky fracture, earthy lustre, slightly to dominantly very argillaceous, trace amber, firm to moderately hard. SANDSTONE: light brown grey, very fine to occasionally very coarse grained, dominantly fine to medium, angular to subrounded, poorly sorted, very weak silica cement, common light brown argillaceous and silt matrix, quartzose with clear to opaque quartz grains with brown argillaceous staining on some grains, trace black coaly detritus, friable, fair to good inferred porosity, no oil fluorescence. CLAYSTONE: light to dark brown, dominantly medium brown, slightly silty and finely arenaceous in part, very slightly to moderately carbonaceous, trace black coaly flecks, trace amber, soft, very dispersive, non fissile. Note: trace moderately bright yellow mineral fluorescence giving a moderate yellow white crush cut from amber. |