PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 8 Date: 24-10-09

Depth: 1120m Progress: 153m Days from Spud: 8

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 9⅝" at 299m

0600 hrs Update: Drill ahead with 8½" hole at 1164m.

Comments: Drill ahead with 8½" hole to 1100m, wiper trip, coals caving severely - increase mud weight to 10.0ppg prior to drilling ahead with 8½" hole to 1120m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 967-1070 | LaTrobe Group - No Show | TG 0.2-5u C1 99% C2 1% C3+ 0 |
| 1070-1090 | LaTrobe Group - No Show The coal has no natural fluorescence but gives a weak dull light yellow green crush cut fluorescence. The amber has a moderately bright solid light to medium yellow natural fluorescence and gives a weak very slow streaming light yellow cut fluorescence. | TG 0.3-1u C1 99% C2 1% C3+ 0 |
| 1090-1120 | LaTrobe Group - No Show The coal has no natural fluorescence but gives a weak dull light yellow green crush cut fluorescence. The amber has a moderately bright solid light to medium yellow natural fluorescence and gives a weak very slow streaming light yellow cut fluorescence. | TG 0.3-0.8u C1 99% C2 1% C3+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 |  |  |  |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 967-1070 | LATROBE GROUP Sandstone (50%) interbedded with Claystone (40%) and Coal (10%). SANDSTONE: light brown grey, very fine to occasionally very coarse grained, dominantly fine to medium, angular to subrounded, poorly sorted, very weak silica cement, common light brown argillaceous and silt matrix, quartzose with clear to opaque quartz grains with brown argillaceous staining on some grains, trace black coaly detritus, friable, fair to good inferred porosity, no oil fluorescence. CLAYSTONE: light to dark brown, dominantly medium brown, slightly silty and finely arenaceous in part, very slightly to moderately carbonaceous, trace black coaly flecks, trace amber, soft, very dispersive, non fissile. Note: trace moderately bright yellow mineral fluorescence giving a moderate yellow white crush cut from amber. |
| 1070-1090 | LATROBE GROUP Sandstone (50%) interbedded with Claystone (40%) and Coal (10%). SANDSTONE: light brown grey, very fine to pebble, dominantly medium to coarse, subangular to rounded, very poorly sorted, weak silica cement, common light brown argillaceous and silt matrix, quartzose with clear to opaque quartz grains often with minor orange brown staining, trace green grey and black cherty lithics, trace to common black coaly detritus, friable, good inferred porosity, no oil fluorescence. CLAYSTONE: medium to dark brown, often very silty and very finely arenaceous, moderately to very carbonaceous, trace black coaly flecks, soft, very dispersive, non fissile. COAL: medium brown to dominantly black, irregular to blocky fracture, earthy to subvitreous lustre, slightly to very argillaceous, trace amber, moderately hard. The coal has no natural fluorescence but gives a weak dull light yellow green crush cut fluorescence. The amber has a moderately bright solid light to medium yellow natural fluorescence and gives a weak very slow streaming light yellow cut fluorescence. |
| 1090-1120 | LATROBE GROUP Sandstone (60%) interbedded with Claystone (40%) and Coal (Trace). SANDSTONE: very light grey to light brown grey, very fine to grit, dominantly medium to coarse, angular to subrounded, very poorly sorted, weak silica cement, common off white to light brown argillaceous and silt matrix, quartzose with clear to opaque quartz grains, trace green grey and black cherty lithics, trace to common black coaly detritus, friable, good inferred porosity, no oil fluorescence. CLAYSTONE: medium brown, often very silty and very finely arenaceous, moderately carbonaceous, trace black coaly flecks, soft, very dispersive, non fissile. COAL: medium brown to dominantly black, irregular to blocky fracture, earthy to subvitreous lustre, slightly to very argillaceous, trace amber, moderately hard. The coal has no natural fluorescence but gives a weak dull light yellow green crush cut fluorescence. The amber has a moderately bright solid light to medium yellow natural fluorescence and gives a weak very slow streaming light yellow cut fluorescence. |