PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 9 Date: 25-10-09

Depth: 1184m Progress: 64m Days from Spud: 9

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 9⅝" at 299m

0600 hrs Update: Continue RIH, drill ahead with 8½" hole at 1204m.

Comments: Drill ahead with 8½" hole to 1184m, POOH for new bit, RIH.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1120-1184 | LaTrobe Group - No Show The coal has no natural fluorescence but gives a weak dull light yellow green crush cut fluorescence. The amber has a moderately bright solid light to medium yellow natural fluorescence and gives a weak very slow streaming light yellow cut fluorescence. | TG 0.1-0.3u C1 99% C2 1% C3+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 |  |  |  |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1120-1184 | LATROBE GROUP Sandstone (50%) interbedded with Claystone (50%) and Coal (Trace). SANDSTONE: very light grey to light brown grey, very fine to granular, dominantly medium to coarse, angular to subrounded, very poorly sorted, weak to moderate silica cement, common off white to light brown argillaceous and silt matrix, quartzose with clear to opaque quartz grains, trace green and black cherty lithics, trace to common black coaly detritus, friable, good inferred porosity, no oil fluorescence. CLAYSTONE: off white to medium brown, very silty and very finely arenaceous in part, kaolinitic in part, slightly to moderately carbonaceous, trace black coaly flecks, trace micromica, firm, very dispersive and washing from samples, non fissile. COAL: medium brown to dominantly black, irregular to blocky fracture, earthy to subvitreous lustre, slightly to very argillaceous, trace amber, moderately hard. The coal has no natural fluorescence but gives a weak dull light yellow green crush cut fluorescence. The amber has a moderately bright solid light to medium yellow natural fluorescence and gives a weak very slow streaming light yellow cut fluorescence. |