The following equipment specifications are for the Hunt Rig 2, which was used to drill Wombat-4.

| DRAWWORKS: | Mac Model-400 (500 Hp) |
| --- | --- |
|  | Single Drum Drawworks S/N 5-20-81. |
|  | Lebus 1-1/8” Main Drum Grooving. |
|  | Recently installed Hydraulic Operated Makeup and Breakout Catheads fitted with Tong Line Torque Gauge. |
|  | Parmac 22” Single Rotor Hydromatic Brake |
|  | 2 Engine Compound & Drillers Console, Master skidded. |
|  | Powered by 2 x Skid/Floor Mounted Caterpillar Model 3406-TA air start diesel engines, F-11524-TC1 Twin Disc Torque Converters with Airflex 16-CB-500 Clutches. Motor Rating: 275 Hp at 1800 rpm each. |
|  | Engine s/n 90U14147 & 90U14162 |
| RIG CAPACITY: | Drilling Depth 2,300+ mtrs with 4-1/2" Drill Pipe |
| SUBSTRUCTURE: | Box type, (G.L. to K.B. 14.00ft,) 11’ High (below rotary) x 18’ Wide x 40 Foot Long, fitted with all necessary & Certified Cross Braces and Rotary support beams |
|  | 8' load skids for one piece rig moving |
|  | Mudline manifold (4”), 36” folding walkways, stairways, hand rails and Drillers House (Dog house) |
| DERRICK: | Al Hicks Model AH-100. Ground Height 100’, Pen |
|  | Type Cantilever Mast, 14 feet 9-3/4” leg Span. |
|  | Maximum static hook load 300,000 lb with 8 lines |
|  | Racking capacity for 4-1/2" Drillpipe |
|  | 6000-ft with 600-ft Bottom Hole Assy. |
| CROWN BLOCK: | Al Hicks Model AHC-300, 5 x 1-1/8” Sheaves including fast line and dead line sheaves. |
| CROWN-O-MATIC: | Koomey Mdl-TCB Crown Block Safety Device. |
| FLOOR WINCH | Ingersol Rand HU Series |
| TRAVELING BLOCK: | Sowa Model S-150-4 , 150 Ton, 4 x 1-1/8” Sheave Unitized Block c/w BJ Model 5150 Hook. |
| ROTARY SWIVEL | Tri-Service Machine Model TSM-150 Swivel 150 ton Rating @ 100 RPM |
| ROTARY TABLE: | Oilwell Mdl-175, (17-1/2”), oil bathe, c/w Varco “MSS” split Master Bushings. |
| MUD PUMP: | No.1 |
|  | 1 x TSM 500 c/w Emsco DA500 Matco FLuid End (7-1/2" x 16") Duplex Mud Pump, Oteco 2" SRV, Belt driven By Caterpillar D-353-E Diesel Engine, Hydril K-10 3000lb Pulsation Dampner, Twin Disc PTO, Oilfield Skid Mounted. |
| MUD PUMP: | No.2 |
|  | 1 only CSF-500 Oilfield skid mounted Tri-plex pump powered by Cummins KTA-19 (600HP) diesel engine c/w Twin Disc SP314P1 Torque converter, 3" SR Valve, K-10 Hydril style pulsation dampner and 3 x 2 Mission charge pump. |
| STANDPIPE: | Standpipe Manifold - 4” x 5000 Lb |
|  | Fitted with Demco 4” Gate Valve |
|  | 1 only 3” ID x 55 ft x 4000/8000 psi Kelly Hose. |
| MUD SYSTEM: | 2 x 300 Barrel Tanks incorporating 80 bbl pill tank and 40 bbl Trip tank. |
| SHAKER: | 2 X D.F.E Linear motion SCR-01 Single three screen shakers. |
| AGITATOR: | Lightnin 72Q7.5 Mixer c/w 25hp Exp Motor |
| DEGASSER: | 48” Mud Gas Separator Vertical Skid Mounted |
| DESILTER: | Harrisburg Mdl 600-12 (600 GPM) |
|  | 12 x 4” Cone Assy, with Mission 6 x 8 centrifugal Pump driven by 50 Hp Electric Motor. |
| DESANDER: | Harrisburg style 2 x 10” Poly type Cones with 6 x 8 Centrifugal Pump driven by 50 Hp Electric Motor. |
| MUD MIXING: | Demco Style Hopper charged by 6 x 8 Centrifugal pump driven by 50 Hp Electric Motor. |
| BLOWOUT PREVENTORS: | 2 only Shaffer 11" 3000 LWS Type Single Gate Ram BOP c/w ram sizes CSO, 2-7/8", 3-1/2", 4-1/2" & 7" |
|  | Annular BOP: |
|  | 1 only Shaffer 11" 3000 Spherical Annular BOP |
| ACCUMULATOR: | Ross Hill G-180-E-20-2-AG (8 station) 180 gallon Accumulator with 1 x Triplex pump c/w 20hp 60HZ Electric motor fitted with 2 only Haskel GW35 56:1 ratio backup Air Pumps c/w remote Drillers console skid mounted. |
| CHOKE MANIFOLD: | 1 x Cameron Skid Mounted Manifold Consisting of: |
|  | : 7 x 2-1/16” x 3000 Cameron Gate Valves |
|  | : 2 x CPI 2-1/16” x 5000 Adjustable Chokes. |
|  | : 1 2-1/16 x 3 M x 5M Tees/Crossovers and manifolding. |
| KILL LINE: | 1 x 3-1/8 x 3000 Cameron manual valve |
|  | 1 x 3-1/8 x 3000 Cameron HCR Vlave |
|  | Continental Emsco XHP series 2” 15000 WP swivel lines |
| INSTRUMENTATION: | Martin Decker 7 Pen Record-O-Graph. |
|  | Martin Decker “Clipper” Weight Type Indicator. |
|  | Martin Decker GM-6 Series Mud pressure System. |
|  | Martin Decker Pump Stroke Indicators. |
|  | Totco TS Rotary Tong Torque System. |
| MUD MONITORING: | AOI-300 Series Flow Indicator System |
|  | AOI Digital Read Out Stroke Counter |
|  | AOI-1000 Series Pnuematic Mud Monitoring System |
| SURVEY UNIT: | Totco Operating Unit No. 6 (P/N ABA8AT5N9) |
|  | Double recorder 0-8 degree. Go-devil series |
|  | 1-5/8” OD x 1-1/4” ID. |
| PIPE SPINNER: | Varco SSW10 Pnuematc |
| KELLY SPINNER: | Gill Model 100 Pnuematic |
| KELLY: | 1 x 4 ¼” Square x 40 ft Kelly with 6-5/8” Reg LH Box up and 4” FH Pin Down. |
| UPPER KELLY | M&M Upper Kelly Cock 6-5/8” Reg LH Pin/Box |
| VALVE: | Connection 10,000 psi test. |
| LOWER KELLY | M and M. 4-1/4” x 10000 (4”IF Pin/Box) Canister |
| VALVE: | Type Lower Kelly Cock. |
| STABBING VALVE: | Flocon (4” IF ) 6-3/8" OD S/N 700073 |
| KELLY DRIVE | Varco 4-1/4” HDS |
| BUSHING: |  |
| DRILLPIPE: | 200 joints 4-1/2" Grade 'E' 16.6 lbs/ft Range 2 |
|  | Drillpipe with 4" if pin/box connections. |
| H.W.D.P: | 6 each 4-1/2" HWDP |
| DRILL COLLARS: | 3 each 8” OD Spiral x 2-13/16 x 29 ft |
|  | 1 each 8” OD Spiral (6 ft ) Pup Joint. |
|  | 26 each 6 ¼” OD Spiral & Slick x 2 13/16 ID x 30 Ft |
|  | Slip recess only, with 4”IF pin/Box connections. |
| FISHING TOOLS: | As required to fish Contractor's String |
| HANDLING TOOLS: | Elevators: |
|  | 1 set 4-1/2” Drillpipe (18 deg) 250t |
|  | 1 set 7” Casing Single Jt |
|  | 1 set 9-5/8” Casing Single Jt |
|  | 2 sets 7” Casing Side Door |
|  | 1 set 9-5/8” Casing Side Door 150t |
|  | 1 set 3-1/2” Drillpipe (18deg) |
|  | 1 set 13-3/8" Casing Side Door |
|  | 1 set 2-3/8" Tubing |
|  | 1 set 2-7/8" Tubing |
|  | Slips: |
|  | 1 set 2-7/8" to 3-1/2” Drillpipe |
|  | 1 set 4-1/2” Drillpipe |
|  | 2 set 6-1/2’ Drill Collar |
|  | 1 set 7” Casing |
|  | 1 set 9-5/8” Casing |
|  | 1 set 13-3/8” Casing. |
|  | Safety Clamp |
|  | 1 x Bassh Ross Type “C” drill collar Dog Clamp |
|  | 1 x Varco MP-R Safety Clamp |
|  | Main Floor RotaryTongs |
|  | 1 set (2) BJ Type “B” Rotary Pipe Tongs. |
|  | Range: 2-3/8” to 13-3/8” |
|  | 1 only Weatherford Model 16K Hydraulic Casing Tong c/w 5-1/2”, 7”, 9-5/8”, 13-3/8” Jaws & Deutz 6cyl Hydraulic Power Pack |
|  | 1 Hillman Kelly 3700H Hydraulic Tubing Tong c/w 2-3/8”, 2-7/8” & 3-1/2” Jaws |
|  | Chain Tongs |
|  | 1 set (2) 9-5/8” Casing Chain Tongs. |
| SUBS: | Bit Subs |
|  | 1 only 6-5/8" Reg Box with float bore x 6-5/8" Reg Box |
|  | 3 only 4-1/2" Reg Box with float bore x 4" IF Box |
|  | 1 only 3-1/2" Reg Box with float bore x 3-1/2" IF Box |
|  | 1 only 7-5/8" Reg Box x 6-5/8" Reg Box |
|  | Pick Up Subs |
|  | 2 only 6-5/8" Reg |
|  | 10 only 4" IF |
|  | 6 only 3-1/2" IF |
|  | X-over Subs |
|  | 6-5/8” Reg Pin x 4” IF Box Bottle Neck |
|  | 2 only 4" IF Pin x 3-1/2" IF Box |
|  | Saver Subs |
|  | 3-1/2" IF Pin x 4" IF Box (6-3/8"OD) |
|  | 3-1/2" IF Pin x 3-1/2" IF Box |
|  | 4” IF Pin x 4" IF Box |
| CASING/TUBING | 9 5/8’’ Casing drift |
| DRIFTS: | 7” Casing drift |
| CUP TESTER: | 9 5/8” Cameron Casing Cup Type |
| WIRELINE UNIT: | HE-V-20-10-HP Hydraulic Wireline Unit |
|  | Capacity : (0.92 x 10,000 ft) |
| WELDING | 1 x Lincoln AS-400-50 Diesel Powered Electric Welder. |
| EQUIPMENT: | 1 only BOC Electric portable 250amp |
| AIR COMPRESSORS: | 1 only Compair model 6050 Rotary screw compressor - operating |
|  | 1 only Compair model 6050 Rotary screw compressor - back up |
|  | 1 only John Wood Co 200psi air receiver Serial # 500803-71 |
| HYDRAULIC POWER SUPPLY: | Flodraulic 100gal, 37kw, 40gpm Hydraulic power unit |
| AC GENERATORS: | 2 only Caterpillar SR4 alternator Powered by Cat-3406PC 256 KVA output |
| FUEL TANKS: | 250 Gallon day tank |
|  | 2 only Ebara model 120/07 50HZ IP55 Fuel pumps |
| WATER TANKS: | 200 bbl |
| PIPE RACKS: | 4 sets 42” High x 28Ft Long Triangle style pipe racks. |
| PIPE BINS: | 3 skid mounted bins . |
| CATWALKS: | 2 x 22’ (45’ overall length) |
| MUD LAB: | Bariod No. 821 Mud Laboratory Kit. |
| MUD SAVER: | Katch Kan model KK001 |
| RAT HOLE DIGGER: | 1 x Tri Service Machine Model-RHD |
|  | Chain/Sprocket driven (1-1/4” Single) |
| CELLAR PUMP: | Cellar Jet via mud pump / Wilden diapragm pump |
| WATER PUMP: | 3” portable water pump with 3” Suction and lay-flat to suit. |
| MECHANIC SHOP: | Oilfield skid mounted workshop / Compressor house containing Electric welder, Drill press, hand and power tools. |
| PRESSURE CLEANER: | Spitwater Model 201 |
| PAYLOADER: | Caterpillar 966C rubber tyred loader. Rated @ 8 tonne Equipped with 7’ tynes & 4m3 bucket. Serial # 78G2032M Arr # 3Y2908 |
| RIG VEHICLES: | 1 x Toyota HJ-75 Station Wagon (Crew) |
|  | 1 x Toyota HJ-75 (1- ton) pick-up UTE. |
| RIG | Toolpusher Accommodation - |
| ACCOMMODATION: | 1 x Transportable unit 40' x 9' x 9' c/w Sleeping quarters - |
|  | Ablution facilities & two separate offices. |
|  | Drilling Supervisors Accommodation - |
|  | 1 x Transportable unit 40' x 9'x 9' c/w Sleeping quarters - |
|  | Ablution facilities & two separate offices. |
| FIRE EXTINGUISHER: | Certified Units located in strategic positions in and around the Rig and Camp. |
| COMMUNICATIONS: | 1 x V-Sat telephone and internet communication system |
|  | 1 x S-3000 Satellite Telephone (Optus) with fax |
|  | 1 x Digital Mobile |
|  | 1 x Iridium mobile Satellite phone |
| CAMP |  |
| GENERATOR: | 1 only Camp Generator House (fully sound proofed) |
|  | ( 12.0 x 3.0m Skid Mounted) c/w |
|  | 14,000 litre capacity water tank -Davey Water Pump |
|  | 2 only Onan Generator sets 100KVA |
|  | Fuel tank capacity 7000 lts |
| SLEEPING UNITS: | 1 only ( 14.4 x 3.0m skid mounted) 6 person Bunkhouse c/w Built in wardrobes, table, beds and bedding. |
|  | 2 only ( 14.4 x 3.0m skid mounted) 10 person Bunkhouse c/w Built in wardrobes, table, beds and bedding. |
| KITCHEN-DINING: | 1 only Kitchen/Diner/Coolroom/Freezer Unit ( 14.4 x 3.0m skid Mounted) Built-in combined freezer/chiller unit c/w Commercial Kitchen Range/Oven, Microwave, Deep fryer, Mixer/Blender, Bain Marie, fixed tables, chairs and all necessary utensils. |
| RECREATION: | 1 x Recreation Room / Clinic Unit |
|  | ( 14.4 x 3.0m Skid Mounted) c/w television, video & lounge chairs |
|  | 1 x First Aid Room |
| ABLUTION: | 1 x Ablution / Laundry / Store Unit |
|  | ( 14.0 x 3.0m Skid Mounted) c/w 315 litre hot water unit, 4 x toilet bays and 5 shower bays. |
|  | Laundry c/w 2 x washing machines & 2 x dryers |
|  | Storage area with built in shelving |