LAKES OIL N.L.

A.C.N. (004 247 214)

Patrobus No.1		PEP 155 (east)

DAILY GEOLOGICAL REPORT No. 10	Date: 02 Oct 05

Depth: 232m		Progress: 0m		Days from Spud: 26

Rig:			Drilltec		GL(ASL):		31.55m

Drilling Rep:	Tim O’Brien	RT (AGL):		0.80m

Geologist:		Ingrid Campbell	Last Casing:         115mm at 232m

Comments: Run and cement 115mm casing to 232m

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
|  | No new formation drilled |  |

| Formation Tops: | Prognosed (mGL) | Actual٭ (mGL) | Actual٭ (mSS) | Difference٭ (High/Low) |
| --- | --- | --- | --- | --- |
| Pleistocene dune deposit | Absent | Surface | +31.55 | - |
| Haunted Hills Gravel | Surface | 34.45 | -2.9 | 34.45 Low |
| Jemmy’s Point Formation | 15 | 45 | -13.45 | 30 Low |
| Gippsland Limestone | 50 | 120 | -88.45 | 70 Low |
| Lakes Entrance Formation | 190 | 226 | -194.45 | 36 Low |
| Colquhuon Gravels | 360 |  |  |  |
| Granite Basement | 400 |  |  |  |
| Total Depth | 600 |  |  |  |

٭Provisional, based on mudlog

LAKES OIL N.L.

A.C.N. (004 247 214)

Patrobus No.1		PEP 155 (east)

DAILY GEOLOGICAL REPORT No. 10

Lithological and Fluorescence Description

| Interval (m) | Description |
| --- | --- |
|  | No new formation drilled |

LAKES OIL N.L.				CUTTINGS DESCRIPTIONS

WELL NAME: 		Patrobus No.1		DATE 01 OCT 05

GEOLOGIST:		Ingrid Campbell		PAGE:	1

| Interval (m) | % | Description |
| --- | --- | --- |
|  |  | No new formation drilled |